| United States Environmental Protection Agency Contract No. GS-35F-4461G SDWIS Project Product Control No. SAIC-SDWIS-2WIP161 October 15, 2010 | Revised Ground Water Rule (GWR) Data Entry Instructions with Examples |
| --- | --- |

This page is intentionally left blank

Revised Ground Water Rule (GWR)

Data Entry Instructions with Examples

CONTRACT NO. GS-35F-4461G

SDWIS PROJECT

Prepared for:

United States Environmental Protection Agency

Office of Ground Water and Drinking Water

Drinking Water Protection Division

1200 Pennsylvania Ave., NW

Washington, DC 20460

Contracting Officer Representative:

Clint Lemmons

Prepared by:

SAIC Solutions Delivery Center

Science Applications International Corporation

8301 Greensboro Drive

MailStop: E-11-2 (Room 11139)

McLean, VA 22102

This page is intentionally left blank

CONTENTS

1.0	Federally Reported Violations	2

2.0	Violation Detail for GWR	3

3.0	Violation Examples	9

Example #1 – Failure to Maintain Microbial Treatment	9

Example #2 - Failure to Maintain Microbial Treatment	9

Example #3 - Failure to Provide Treatment for Multiple Sources	10

Example #4 - Failure to Complete Significant Deficiency Corrective Action Interim Step	13

Example #5 - Failure to Address Multiple Significant Deficiencies	14

Example #6 - Failure to Address Contamination	17

Example #7 - Failure to Conduct Required Source Water Assessment Monitoring	19

Example #8 - Failure To Conduct Continuous Residual Disinfectant Monitoring And Failure To Take Grab Samples At GWR Treatment Plant Serving >3,300 People	20

Example #9 - Failure To Conduct Continuous Residual Disinfectant Monitoring But Grab Samples Collected At GWR Treatment Plant Serving >3,300 People	21

Example #10 - PWS without Disinfection Treatment Experiences TCR Total Coliform-Positive Result, Assessment Source Water Monitoring (In Compliance with GWR)	21

Example #11 - Failure to Monitor for Additional Source Water Samples	22

Example #12 - PWS with Disinfection Treatment Experiences TCR Routine, Total Coliform-Positive, Result	24

Example #13 - PWS without Disinfection Treatment Experiences TCR Total Coliform-Positive Result and Fails to Conduct Triggered Source Water Monitoring	24

Example #14 - Failure to Take Required Complete Set of Triggered Source Water Monitoring Samples	26

Example #15 - Failure to Notify Primacy Agency of Failure to Maintain Minimum Disinfection	28

Example #16 - Failure to Notify Primacy Agency of Completion of Corrective Action	30

Example # 17 - Failure to Notify Primacy Agency of Exception to Triggered Source Water Monitoring	31

Example #18 - Failure to Maintain Records	33

Example #19 - Failure to Consult Regarding a Significant Deficiency	34

Example #20 - Failure to Consult with Primacy Agency Multiple Deficiencies	36

Example #21 - Failure to Consult Contamination	38

Example #22 - Sanitary Survey Cooperation Failure	39

Example #23 - Failure to Notify Purchase PWS	41

Example #24 - Failure to Notify Wholesale PWS	42

Example #25 - Public Notification of Violation	44

Example #26 - Public Notice Requested and Received	46

Example #27 - Public Notification of Positive Source Water	47

4.0	Inventory	49

4.1	Outstanding Performers	49

4.2	Treatment Processes	50

4.2.1	Treatment Objective/Processes Applied at PWS	50

4.2.2	Treatment Applied by Seller for a Purchased Water Source	50

4.2.3	Generic Reporting for Sources, Treatment Plants, Flows, Treatments	51

4.2.4	WSF Source, WSF Treatment Plant, Treatment Data, Facility Flows	54

5.0	Other Actions	56

5.1	Sanitary Survey	56

5.1.1	Sanitary Survey Examples	60

Example 1 – Purchase Water System without Treatment or Finished Water Storage	60

Example 2 – Large Ground Water System with Ten Wells with Two Partial Sanitary Surveys not on Consecutive Days	60

5.2	Corrective Actions	62

5.2.1	Event Schedule Activity Examples	63

Example 1 – Significant Deficiency Corrective Actions	63

Example 2 – Fecal Indicator Positive Source	65

EXHIBITS

Exhibit 1: Summary of Federally Reported Violations for the GWR	2

Exhibit 2: Federally Reported Violations for the GWR	4

Exhibit 3 Ex 2: Failure to Maintain Adequate Treatment	10

Exhibit 4 Ex 3-A: Failure to Provide Treatment	11

Exhibit 5 Ex 3-B: Failure to Provide Treatment	12

Exhibit 6 Ex 3-C: Enforcement Object	12

Exhibit 7 Ex 3-D: Enforcement Object	12

Exhibit 8 Ex 4-A:  Failure to Address a Deficiency Violation Object Elements	14

Exhibit 9 Ex 4-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation	14

Exhibit 10 Ex 5-A: Failure to Address a Deficiency	15

Exhibit 11 Ex 5-B: Failure to Address a Deficiency	16

Exhibit 12 Ex 5-C: Enforcement Action Object	16

Exhibit 13 Ex 5-D: Enforcement Action Object	16

Exhibit 14 Ex 6-A: Failure to Address Contamination	18

Exhibit 15 Ex 6-B: Failure to Address Contamination	18

Exhibit 16 Ex 6-C: Enforcement Action Object	19

Exhibit 17 Ex 6-D: Enforcement Action Object	19

Exhibit 18 Ex 7: Failure to Conduct Assessment Source Water Monitoring	20

Exhibit 19 Ex 8: A System Fails to Conduct Compliance Monitoring	21

Exhibit 20 Ex 11-A: Failure to Conduct Additional Source Water Monitoring	23

Exhibit 21 Ex 11-B: Enforcement Action Object	23

Exhibit 22 Ex 13-A: Failure to Conduct Triggered Source Water Monitoring	25

Exhibit 23 Ex 13-B: Enforcement Action Object	25

Exhibit 24 Ex 14-A: Failure to Conduct Triggered Source Water Monitoring	27

Exhibit 25 Ex 14-B: Failure to Conduct Triggered Source Water Monitoring	27

Exhibit 26 Ex 14-C: Enforcement Action Object	28

Exhibit 27 Ex 14-D: Enforcement Action Object	28

Exhibit 28 Ex 15-A: Failure to Notify Primacy Agency of Compliance Monitoring Exceedance	29

Exhibit 29 Ex 15-B: Enforcement Object	29

Exhibit 30 Ex 16-A: Failure to Notify Primacy Agency of Completed Corrective Action	30

Exhibit 31 Ex 16-B: Enforcement Object	31

Exhibit 32 Ex 17-A: Failure to Notify Primacy Agency of Triggered Source Water Monitoring Exception Criteria	32

Exhibit 33 Ex 17-B: Enforcement Object	33

Exhibit 34 Ex 18-A: Failure to Address a Deficiency	33

Exhibit 35 Ex 18-B: Enforcement Object	34

Exhibit 36 Ex 19-A: Failure to Consult Regarding a Deficiency	35

Exhibit 37 Ex 19-B: Enforcement Object	36

Exhibit 38 Ex 20-A: Failure to Consult Regarding Multiple Deficiencies Violation Object Elements	37

Exhibit 39 Ex 20-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation	37

Exhibit 40 Ex 21-A:  Failure to Consult Regarding Fecal Contamination Violation Object Elements	39

Exhibit 41 Ex 21-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation	39

Exhibit 42 Ex 22-A: Sanitary Survey Cooperation Failure	40

Exhibit 43 Ex 22-B: Enforcement Object	41

Exhibit 44 Ex 23-A: Failure to Notify Other PWS	42

Exhibit 45 Ex 23-B: Enforcement Object	42

Exhibit 46 Ex 24-A: Failure to Notify Other PWS	43

Exhibit 47 Ex 24-B: Enforcement Object	43

Exhibit 48 Ex 25-A: Enforcement Object	45

Exhibit 49 Ex 25-B: Failure to Provide Public Notice	45

Exhibit 50 Ex 25-C: Enforcement Object	45

Exhibit 51 Ex 25-D: Enforcement Object	46

Exhibit 52 Ex 26-A: Enforcement Action Object	46

Exhibit 53 Ex 26-B: Enforcement Action Object	46

Exhibit 54 Ex 27-A: Enforcement Object	48

Exhibit 55 Ex 27-B: Enforcement Object	48

Exhibit 56 Ex 27-C: PN Violation without NPDWR Violation	48

Exhibit 57 Ex 27-D: Enforcement Object	49

Exhibit 58: Outstanding Performers Data Elements for Water System Object	50

Exhibit 59: Required Treatment Process Code	50

Exhibit 60: Required Seller Source Treatment Code in WSF Source Object	51

Exhibit 61: Water System Object Element Optionality	52

Exhibit 62: Source WSF Object Element Optionality	52

Exhibit 63: SDWIS/FED Water Sources and Codes	53

Exhibit 64: Purchased Source Seller Source Treatment Code Permitted Values	53

Exhibit 65: Water System Object Elements	54

Exhibit 66: Source Facilities	55

Exhibit 67: Treatment Plant Facilities	56

Exhibit 68: Treatment Data	56

Exhibit 69: Facility Flows	56

Exhibit 70: Site Visit Object Elements	57

Exhibit 71: Site Visit Object	58

Exhibit 72: Visit Agency Type Permitted Values	59

Exhibit 73: Category Evaluation Permitted Values	59

Exhibit 74 Ex 1: Purchase Water System without Treatment or Finished Water Storage Site Visit Object Elements	60

Exhibit 75 Ex 2-A: Visit Object Elements for Large Ground Water System with Ten Wells Reported as First of Two Visits	61

Exhibit 76 Ex 2-B: Site Visit Object Elements for Large Ground Water System with Ten Wells Reported as Second of Two Visits	61

Exhibit 77: Event Schedule Activity Object Elements	62

Exhibit 78: Activity Type Code Permitted Values for GWR	63

Exhibit 79: Reason Code Permitted Values for GWR and Optional Surface Water Corrective Actions	63

Exhibit 80 Ex 1-A: Significant Deficiency Final Corrective Actions Event Schedule Activity Object Elements Reported	64

Exhibit 81 Ex 1-B: Significant Deficiency Interim Corrective Actions Event Schedule Activity Object Elements Reported	64

Exhibit 82 Ex 1-C: Significant Deficiency Interim Corrective Actions Event Schedule Activity Object Elements Reported	64

Exhibit 83 Ex 1-D: Significant Deficiency Completed Corrective Actions Event Schedule Activity Object Elements Reported	65

Exhibit 84 Ex 2-A: Fecal Indicator Positive Source Scheduled Corrective Actions Event Schedule Activity Object Elements Reported	65

Exhibit 85 Ex 2-B: Fecal Indicator Positive Source Scheduled Corrective Actions Event Schedule Activity Object Elements Reported	66

Exhibit 86 Ex 2-C: Fecal Indicator Positive Source Completed Corrective Actions Event Schedule Activity Object Elements Reported	66

Exhibit 87 Ex 2-D: Fecal Indicator Positive Source Completed Corrective Actions Event Schedule Activity Object Elements Reported	66

Safe Drinking Water Information System (SDWIS)

Reporting Under the GWR

The Safe Drinking Water Act (SDWA) requires states to report drinking water information periodically to EPA.  Safe Drinking Water Information System, Federal Version (SDWIS/FED) is the EPA national database that receives all Primacy Agency routine data submittals for the 155,000 Public Water Systems (PWS) and stores and provides the data for user retrieval. EPA uses the data to manage the Public Water System Supervision (PWSS) program; overseeing Primacy Agency activities, performing federal enforcement, providing compliance assistance, providing information to rule makers about the characteristics of the regulated community for input into rule development and evaluation, responding to public inquiries and providing information about the status of rule implementation.  Primacy Agencies, mostly State environmental or health agencies, perform the day-to-day activities to implement the regulations and regulate the drinking water systems within their jurisdictions to ensure that each PWS meets state and EPA standards for safe drinking water.  Primacy Agencies report the following information routinely to EPA:

- Basic information on each water system, such as water system name, ID number, number of people served, type of system (year-round or seasonal), the source(s) of water (ground water and surface water) and treatments provided;

- Violation information for each water system; where it has failed established  monitoring and reporting schedules, failed to comply with mandated treatment techniques, or exceeded any maximum contaminant levels (MCLs) or other standards;

- Enforcement information including the  actions Primacy Agencies have taken to ensure that drinking water systems return to compliance when in violation of a drinking water regulation; and,

- Sampling results for unregulated contaminants and for regulated contaminants when the monitoring results exceed the MCL.

In most cases, the PWS rule violations that Primacy Agencies report to EPA is a summary of the actual violation details.  For example, there are many detailed water quality monitoring requirements needing to be met by PWSs, such as sampling locations, number of samples taken, use of certified laboratories and use of specific analysis methods, as well as reporting schedules for reporting data to Primacy Agencies.  PWSs that fail one or more of these requirements will have incurred a routine monitoring and reporting violation.  EPA has determined that detailed data, specifically the exact activity that was failed need not be reported for each noncompliant PWS, just a single routine monitoring and reporting violation.  However, Primacy Agencies and PWSs must maintain details of noncompliance events based upon PWS and Primacy Agency Record Keeping requirements identified in the rules, as well as sufficient information from which to ensure that mitigation of noncompliance is tracked to its completion.  In fact, Primacy Agencies are required to report data identifying that noncompliance has been “returned to compliance” for many of the violations reported to EPA.

EPA’s SDWIS/FED data system is composed of several parts.  SDWIS/FedRep is an application that Primacy Agencies use to manage routine data submittals to EPA; validating data, managing errors found, and communicating the results to EPA regional offices.  EPA’s Central Data Exchange (CDX), part of EPA’s National Environmental Information Exchange Network (NEIEN), is used to transfer data from Primacy Agencies to EPA, and for Primacy Agencies to retrieve output reports resulting from additional data validations.  SDWIS Operational Data System (SDWIS/ODS) is a database that receives, processes and stores data from Primacy Agency data submittals.  SDWIS Data Warehouse periodically downloads data from SDWIS/ODS, adds additional data fields to better characterize data, and provides the data for end user retrievals as well as for the Standard Reports available through SDWIS/Reporting Services.

# Federally Reported Violations

Violations of the Ground Water Rule (GWR) include treatment technique (TT) violations and monitoring and reporting (M&R) violations as well as those categorized as “other”, as summarized in Exhibit 1, “Summary of Federally Reported Violations for the GWR.”  Exhibit 2, “Federally Reported Violations for the GWR,” provides guidance about the data fields that need to be reported for each of the violations.

| Exhibit 1: Summary of Federally Reported Violations for the GWR |
| --- |
| Violation Code | Contaminant Code | Violation Category | Violation Name | Initial Compliance Date |
| Health-based Violations |
| 41 | 0700-GWR | TT | Failure to Maintain Microbial Treatment | 12/01/2009 |
| 42* | 0700-GWR | TT | Failure to Provide Treatment | 12/01/2009 |
| 45* | 0700-GWR | TT | Failure to Address a Deficiency | 12/01/2009 |
| 48* | 0700-GWR | TT | Failure to Address Contamination | 12/01/2009 |
| Monitoring and Reporting (M/R) Violations |
| 19 | 3002 Enterococci 3014 E. Coli or 3028 Coliphage | MR | Monitoring, GWR Assessment Source Water | 12/01/2009 |
| 31 | 0700-GWR | MR | Monitoring of Treatment (Unfilt/GWR) | 12/01/2009 |
| 34 | 3002 Enterococci 3014 E. Coli or 3028 Coliphage | MR | Monitoring, GWR Triggered/Additional | 12/01/2009 |
| Other Violations |
| 05* | 0700-GWR | Other | Notification, State | 12/01/2009 |
| 09* | 0700-GWR | Other | Record Keeping | 12/01/2009 |
| 20* | 0700-GWR | Other | Failure to Respond/Consult with State | 12/01/2009 |
| 28* | 0700-GWR | Other | Sanitary Survey Cooperation Failure | 12/01/2009 |
| 73* | 0700-GWR | Other | Failure To Notify Other PWS | 12/01/2009 |
| 75* | 7500-PN Rule | Other | PN Violation for an NPDWR Violation |  |
| 76* | 7500-PN Rule | Other | PN Violation without NPDWR Violation |  |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX  along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

# Violation Detail for GWR

Exhibit 2 contains the federally reportable violations for the GWR in more detail. These violations are listed by requirement and violation type. Exhibit 2 includes the SDWIS/FED reporting codes, the regulatory citation, and a name (in italics) & detailed description of the violation. Examples of reporting these violations to EPA’s SDWIS/FED follow.

There are two separate violation uniqueness checks in SDWIS/FED, duplicate by ID and duplicate by data.  Once a violation passes the duplicate by ID check and is created in SDWIS/FED, it is subject to the second “duplicate by data” check.  This edit check ensures the violation being processed does not already exist in SDWIS/FED for the same PWS + Violation Type + Contaminant Code + Compliance Period Begin Date.

Several GWR requirements are initiated by the notification of the PWS of a sample result or deficiency.  Since the PWS may be notified of more than one precipitating sample result or deficiencies on the same day, failure to take appropriate actions may result in multiple violations with the same Compliance Period Begin Date.  Therefore, the GWR violation reporting requirements for some violation types necessitate an expansion of the SDWIS/FED violation duplicate-by-data criteria to include the underlying object identifier, similar to the way the original underlying violation ID is part of the “duplicate by data” check for type 75 public notice violations.

The existing violation data element, PUBLIC NOTICE UNDERLYING VIOLATION ID, will be renamed UNDERLYING OBJECT ID and expanded from 20 to 40 characters in length.  A new data element, UNDERLYING DATA TYPE, will be used to distinguish the type of underlying object.  The following are the initial enumerated values for the UNDERLYING DATA TYPE.

- PNORIGVIOL - Underlying PN Violation ID

- CORACTION - Corrective Action Event Schedule Activity ID

- SMPLRESULT - Precipitating Sample Analytical Result ID

SDWIS/FED edit checks will ensure when the UNDERLYING DATA TYPE equals PNORIGVIOL, the UNDERLYING OBJECT ID matches a Violation ID for the specified PWS in the database.  Likewise, when the UNDERLYING DATA TYPE equals CORACTION, the UNDERLYING OBJECT ID matches a corrective action type of Event Schedule Activity ID for the specified PWS.  Precipitating sample analytical results will not be reported.  When the UNDERLYING DATA TYPE equals SMPLRESULT, the UNDERLYING OBJECT ID will uniquely match a sample analytical result which can be identified by the Primacy Agency and has not been reported to SDWIS/ODS.

| Exhibit 2: Federally Reported Violations for the GWR |
| --- |
| Affected Violation/Citation | SDWIS Violation Code | Contaminant Code | Compliance Period Begin Date | Compliance Period End Date | Major Violation, Severity Indicator, and Underlying Object |
| Health-Based Violations |
| Failure to Maintain Microbial Treatment - Failure to maintain at least 4-log treatment of viruses and operate according to Primacy Agency requirements. CFR §141.404(c) | 41 | 0700-GWR | First day of monthly monitoring period | Last day of monthly monitoring period | Do Not Report |
| Failure to Provide Treatment - Failure to install treatment in response to a positive source water sample, including failure to satisfy Primacy Agency specified schedule. CFR §141.404(b), 141.403(a)(6)(iv) | 42 | 0700-GWR | First day after treatment must be installed which is the appropriate date defined as either; the State specified schedule, including interim steps, or 120 days of receiving written notification of fecal indicator positive which requires installation of treatment. | Do Not Report* | Major Indicator And Severity: Do not Report Underlying Object: Report Unique Corrective Action ID Underlying Data Type: CORACTION |
| Failure to address a deficiency - Failure to take a corrective action in response to a sanitary survey deficiency within 120 days, including failure to satisfy State specified schedule. CFR §141.404(a) | 45 | 0700-GWR | First day after the appropriate date defined as either the State specified schedule which the PWS failed to meet, including interim steps, or 120 days from the date of the notification of significant deficiency. | Do Not Report* | Major Indicator And Severity: Do not Report Underlying Object: Report Unique Corrective Action ID Underlying Data Type: CORACTION |
| Failure to address contamination - Failure to take a corrective action in response to a fecal indicator positive sample within 120 days, including failure to satisfy State specified schedule. CFR §141.404(a) | 48 | 0700-GWR | First day after the appropriate date defined as either the State specified schedule which the PWS failed to meet, including interim steps or120 days from the date of the notification of fecal contamination. | Do Not Report* . | Major Indicator And Severity: Do not Report Underlying Object: Report Unique Corrective Action ID Underlying Data Type: CORACTION |
| Monitoring and Reporting Violations |
| Monitoring, GWR Assessment Source Water - Failure to conduct source water monitoring A system that fails to conduct assessment source water monitoring as required. CFR §141.402(b) | 19 | 3002 Enterococci, 3014 E. Coli or 3028 Coliphage | First day of monitoring period as specified by the Primacy Agency | Last day of monitoring period as specified by the Primacy Agency | Major Indicator: Required Major: No samples collected. Minor: Some but not all samples collected. Severity and Underlying Object: Do Not Report |
| Monitoring of Treatment (SWTR-Unfilt/GWR) - Failure to conduct or report compliance monitoring at a GW treatment plant (with 4-log treatment of viruses under CFR § 141.403(b)) or unfiltered SW treatment plant | 31 | 0700-GWR | First day of monthly monitoring period | Last day of monthly monitoring period | Major Indicator: Required Major: < 90% samples collected. Minor: >=90% samples collected Severity and Underlying Object: Do Not Report |
| Monitoring, GWR Triggered/Additional – Failure to conduct source water monitoring A system that does not provide 4-log treatment of viruses and fails to conduct either triggered or additional source water monitoring as required. CFR §141.402(a)(1) and 141.402(a)(3) | 34 | 3002 Enterococci, 3014 E. Coli or 3028 Coliphage | First day after monitoring period | Do Not report * | Major: No samples collected. Minor: Some but not all samples collected. Severity: Do not Report Underlying Object: Report Unique Sample Results ID Underlying Data Type: SAMPRESULT |
| Other Violations |
| Failure to notify primacy agency - Failure to notify the Primacy Agency of failure to meet primacy agency specified compliance monitoring requirements, completion of corrective action, or criteria for exception to triggered monitoring. CFR §141.405(a)(1), 141.405(a)(2) and 141.405(a)(3) | 05 | 0700-GWR | First day after the failure to notify the primacy agency on the next business day after failure to meet primacy agency compliance monitoring requirements or 30 days after completion of corrective action or meeting exception criteria for triggered source water monitoring. | Do Not report * | Do Not Report |
| Failure to maintain records - Failure to document and maintain records for specified period of time. CFR §141.402(b) | 09 | 0700-GWR | First day after the system fails to keep records. | Do Not report * | Do Not Report |
| Failure to address a deficiency - Failure to consult with State in response to a sanitary survey deficiency within 30 days of notification. CFR §141.404(a) Failure to address contamination - Failure to consult with State in response to a fecal indicator positive sample within 30 days of notification under CFR §141.404(a) | 20 | 0700-GWR | First day after the failure to consult with the Primacy Agency defined as 30 days from the date of the notification of either significant deficiency or fecal contamination | Do Not Report* . | Do Not Report |
| Sanitary Survey Cooperation Failure - Failure to provide the State, at State's request, any existing information that may enable State to conduct a sanitary survey. CFR §141.401(a) | 28 | 0700-GWR | First day after information was due at Primacy Agency | Do Not Report* | Do Not Report |
| Failure to notify other PWS - Failure to notify consecutive systems, either wholesale or purchase, when positive sample results found under CFR §141.402(a)(4) | 73 | 0700-GWR | First day after PWS fails to provide notification of positive sample result | Do Not Report* | Do Not Report |
| PN Violation for a NPDWR Violation - Failure to provide Public Notice when a violation of GWR occurs under CFR §141.202 | 75 | 7500-PNR | First day after PWS fails to provide notification of violation or submit proof to Primacy Agency | Do Not Report* | Major Indicator And Severity: Do not Report Underlying Object: Report Unique Original Violation ID Underlying Data Type: PNORIGVIOL |
| PN Violation without NPDWR Violation - Failure to provide Public Notice when a source water fecal indicator positive occurs under CFR §141.402(g) | 76 | 7500-PNR | First day after PWS fails to provide public notification or submit proof to Primacy Agency | Do Not Report* | Do Not Report |

*These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

# Violation Examples

The following examples illustrate GWR violation scenarios; explain whether a violation has occurred, and if so, show the violation and enforcement action details to be reported by the Primacy Agency to EPA.

### Example #1 – Failure to Maintain Microbial Treatment

Failure to maintain at least 4-log treatment of viruses and operate according to State requirements

CFR §141.404(c)

Violation Type = 41-Failure to Maintain Microbial Treatment

Contaminant Code = 0700-GWR

PWS, PA1234567, is a community GWS serving 8,500 people.

- The system has two wells in use year-round and notifies the Primacy Agency in March, 2009 that it provides 4-log treatment of viruses before the first customer.

- On 01/22/2011 (a Saturday), the chlorine residual at the entry point drops below the required level set by the Primacy Agency.  The operator determines that due to a malfunctioning chlorine pump, the system has not been providing 4-log treatment of viruses at one of its wells.

- The PWS operator corrects the problem within an hour of the initial drop in chlorine residual.

- In addition, the system officially notifies the Primacy Agency of its failure to consistently provide 4-log treatment of viruses with its monthly operating report to the Primacy Agency on 02/01/2011.

The PWS was not in violation as the problem was corrected within 4 hours of determining that the 4-log treatment of viruses is not being maintained.

### Example #2 - Failure to Maintain Microbial Treatment

Failure to maintain at least 4-log treatment of viruses and operate according to State requirements

CFR §141.404(c)

Violation Type = 41-Failure to Maintain Microbial Treatment

Contaminant Code = 0700-GWR

This scenario uses the same situation as in Example #1 , except the operator is unable to correct the malfunctioning chlorine pump for an additional week; therefore 4-log treatment can not be maintained for that week.  In this situation, the PWS notifies the Primacy Agency of the failure to maintain the minimum chlorine residual on the next business day, 01/24/2011.

The PWS is in violation of the treatment technique requirements set forth by the Primacy Agency for the month of January 2011.  The Compliance Period Begin Date and End Date are 01/01/2011 and 01/31/2011 respectively.  The Primacy Agency must report this violation (Exhibit 3 Ex 2) to EPA using the Violation object with the following data elements and values.

| Exhibit 3 Ex 2: Failure to Maintain Adequate Treatment Violation Object Elements |
| --- |
| Element Name | Data Value |
| PWS ID | PA1234567 |
| Facility ID | Do Not Report |
| Violation ID | 0100121 |
| Violation Type Code | 41 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2011-01-01 |
| Compliance Period End Date | 2011-01-31 |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

### Example #3 - Failure to Provide Treatment for Multiple Sources

Failure to take a corrective action which specifies installation of treatment in response to a positive source water sample from multiple source water facilities to satisfy Primacy Agency specified schedule which specifies installation or modification of treatment.

CFR §141.404(b), 141.403(a) (6) (iv)

Violation Type = 42- Failure to Provide Treatment

Contaminant Code = 0700-GWR

PWS PA7654721 is a non-community GWS serving 8,000 people.

- The system has three wells in use year-round and does not provide 4-log treatment of viruses before the first customer.

- TCR sampling performed during the month of June 2015 resulted in a total coliform-positive (TC+) result.

- The PWS is notified about the TC+ result on 06/10/2015 and performs triggered source water monitoring within 24 hours.

- Fecal indicator-positive (FI+) triggered results from Well #1 and Well #2 were reported to the system.

- The system receives notification that the additional monitoring sample results are FI+ on 06/19/2015.

- The system consulted the Primacy Agency within 30 days and agrees to a corrective action plan to provide a single treatment plant for both sources within 120 days, i.e. by 10/17/2015.

- The PWS did not install treatment by 10/17/2015.

- The PWS returned to compliance on 12/15/2015.

The PWS incurs two violations of the treatment technique requirements of the GWR for failing to meet the Primacy Agency directed corrective action deadline resulting from contamination of a ground water sources.  Even though the plan includes a single treatment plant for both sources; a violation must be reported for each source.   The Primacy Agency must report both violations (Exhibits 4 Ex 3-A and 5 Ex 3-B) to EPA, using the Violation object, Enforcement object, and associated data elements and values.

For both violations, the Compliance Period Begin Date is 10/18/2015 (one day after the first interim step specified by the Primacy Agency to implement a corrective action plan).  The unique IDs for the interim steps (the corrective actions for the source water system facility fecal contamination), which are reported using the Event Schedule Activity object, are 128 and 129. These must be reported as the Underlying Object ID with the Underlying Data Type set to CORACTION for these two violations. These are open-ended violations; and therefore, the Compliance Period End Dates are not reported.

Two scheduled corrective actions must be reported without an Activity End/Achieved Date (Exhibits 84 Ex 2-A and 85 Ex 2-B) with the next quarterly actions report.  In the examples, the Primacy Agency uses the Comment field to identify the source water system facility. Two completed corrective actions must also be reported with an Activity End/Achieved Date (Exhibits 86 Ex 2-C and 87 Ex 2-D) with the next quarterly actions report.

The PWS returns to compliance on 12/15/2015 and the Primacy Agency must report return to compliance enforcement actions (Exhibit 6 Ex 3-C and 7 Ex 3-D) using the Enforcement object and associated data elements and values.

| Exhibit 4 Ex 3-A: Failure to Provide Treatment Violation Object Elements |
| --- |
| PWS ID | PA7654721 |
| Facility ID | Do Not Report |
| Violation ID | 2468975 |
| Violation Type Code | 42 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2015-10-18 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 128 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

| Exhibit 5 Ex 3-B: Failure to Provide Treatment Violation Object Elements |
| --- |
| PWS ID | PA7654721 |
| Facility ID | Do Not Report |
| Violation ID | 2468976 |
| Violation Type Code | 42 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2015-10-18 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 129 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

*These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 6 Ex 3-C: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA7654721 |
| Enforcement ID | 398187444 |
| Enforcement Date | 2015-12-15 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 2468975 |

| Exhibit 7 Ex 3-D: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA7654721 |
| Enforcement ID | 398187445 |
| Enforcement Date | 2015-12-15 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 2468976 |

### Example #4 - Failure to Complete Significant Deficiency Corrective Action Interim Step

Failure to take a corrective action in response to a sanitary survey deficiency within 120 days, including failure to satisfy State specified schedule.

CFR §141.404(a)

Violation Type = 45- Failure to Address a Deficiency

Contaminant Code = 0700-GWR

PWS PA2154376 is a non-community GWS serving 800 people.

- The system has one well in use year-round and does not provide 4-log treatment of viruses before the first customer.

- During a sanitary survey on 09/01/2013, the Primacy Agency identifies a significant deficiency—leaking septic tanks close to the system’s well.

- The system is notified of the deficiency on 09/14/2013 in a letter from the Primacy Agency. The letter does not indicate a specific corrective action that the system is required to take.

- As required, the system contacted the Primacy Agency within 30 days of receiving written notice of the significant deficiency and the system and the Primacy Agency developed a plan for implementing corrective action.

- The first step of the corrective action plan was scheduled to be completed by 12/01/2013 with the remainder scheduled to be completed by 10/01/2014.

- The system, however, does not complete the first step of the corrective action plan on time.

- The PWS returned to compliance on 02/25/2014.

The Primacy Agency must report this violation (Exhibit 8 Ex 4-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 12/02/2013 (one day after the PWS was to complete the first Primacy Agency-specified scheduled action).  The unique ID for the interim corrective action, which is reported using the Event Schedule Activity object, is 753. It must be reported as the Underlying Object ID with the Underlying Data Type set to CORACTION for this violation (Exhibit 81 Ex 1-B).  This is an open-ended violation and therefore the Compliance Period End Date is not reported. The PWS returned to compliance on 02/25/2014 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 9 Ex 4-B) using the Enforcement object and associated data elements and values.  The completed interim step Corrective Action will be reported using the Event Schedule Activity object (Exhibit 82 Ex 1-C).

| Exhibit 8 Ex 4-A: Failure to Address a Deficiency Violation Object Elements |
| --- |
| PWS ID | PA2154376 |
| Facility ID | Do Not Report |
| Violation ID | 27474791 |
| Violation Type Code | 45 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2013-12-02 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 753 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

*These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date..

| Exhibit 9 Ex 4-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA2154376 |
| Enforcement ID | 34828023089 |
| Enforcement Date | 2014-02-25 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 27474791 |

### Example #5 - Failure to Address Multiple Significant Deficiencies

Failure to take a corrective action in response to a sanitary survey deficiency within 120 days, including failure to satisfy Primacy Agency specified schedule.

CFR § 141.404(a)

Violation Type = 45- Failure to Address a Deficiency

Contaminant Code = 0700-GWR

PWS PA1093487 is a community GWS serving 1,500 people.

- The system has one well in use year-round.

- During a sanitary survey on 06/01/2013, the Primacy Agency identifies two significant deficiencies—the chlorination room is not explosion proof and lacks any safety equipment and the well casing does not extend above the ground surface.

- The system is notified of the deficiencies on 06/10/2013 in a letter from the Primacy Agency.

- The system is told it does not need to consult with the Primacy Agency.  It must complete corrective actions within 120 days of receiving written notification from the Primacy Agency of the significant deficiencies, which is 10/08/2013.

- By 10/08/2013, the deficiencies have not been corrected.

- The system is notified of its violations on 11/15/2013, for failure to take corrective actions within 120 days of receiving written notice.

- The PWS returns to compliance on 12/01/2013 for the chlorination room deficiency and on 02/07/2014 for the well casing deficiency.

The PWS has incurred two treatment technique violations of the GWR for failing to implement corrective actions within 120 days of notification by the Primacy Agency, one for each of the two significant deficiencies.  The Primacy Agency must report these violations (Exhibits 10 Ex 5-Aand 11 Ex 5-B) to EPA using the Violation object, enforcement action object, and associated data elements and values.  The Compliance Period Begin Date is 10/09/2013 (one day after the date of the significant deficiencies must be addressed).  These are open-ended violations and therefore, the Compliance Period End Date is not reported. Each violation will be associated to the appropriate underlying Corrective Action.   The unique ID for the Event Schedule Activity object for the appropriate corrective actions, 819 and 906, must be reported as the Underlying Object ID with the Underlying Data Type set to CORACTION.  The PWS returns to compliance on 12/01/2013 for the chlorination room deficiency and on 02/07/2014 for the well casing deficiency, the Primacy Agency must report a return to compliance enforcement action for each violation (Exhibits 12 Ex 5-C and 13 Ex 5-D) using the Enforcement object and associated data elements and values.

| Exhibit 10 Ex 5-A: Failure to Address a Deficiency Violation Object Elements |
| --- |
| PWS ID | PA1093487 |
| Facility ID | Do Not Report |
| Violation ID | 158975 |
| Violation Type Code | 45 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2013-10-09 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 819 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

| Exhibit 11 Ex 5-B: Failure to Address a Deficiency Violation Object Elements |
| --- |
| PWS ID | PA1093487 |
| Facility ID | Do Not Report |
| Violation ID | 158976 |
| Violation Type Code | 45 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2013-10-09 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 906 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 12 Ex 5-C: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA1093487 |
| Enforcement ID | 398187943 |
| Enforcement Date | 2013-12-01 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 158975 |

| Exhibit 13 Ex 5-D: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA1093487 |
| Enforcement ID | 398187943 |
| Enforcement Date | 2014-02-07 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 158976 |

### Example #6 - Failure to Address Contamination

Failure to provide treatment as outlined in a corrective action plan specified schedule.

CFR §141.404(b), CFR §141.403(a) (6) (iv)

Violation Type = 48- Failure to Address Contamination

Contaminant Code = 0700-GWR

PWS PA7654321 serves 5,000 people purchasing all its raw untreated water from a wholesaler, PWS PA0001010.

- The wholesaler has 15 wells providing ground water to seven different purchasing PWSs.

- As part of its routine TCR sampling, PA7654321 is notified by its laboratory of a Total Coliform-positive (TC+) sample taken on 05/12/2014.

- In accordance with Section 141.402(a) (4), PA7654321 notifies its wholesaler within 24 hours of having a TC+.

- The wholesaler, PA0001010, must perform triggered source water monitoring within 24 hours of receipt of the notice from PA7654321.

- PA0001010 performs required triggered source water monitoring, and is notified by its laboratory on 05/14/2014 of a fecal indicator-positive (FI+) result on two of its wells, Northside #1 and Northside #2.

- The wholesaler must notify all the consecutive systems served by these sources of the FI+ result, which it does on 05/15/2014.  The wholesaler and seven purchasing systems must all provide public notice within 24 hours of notification, which is 05/15/2014 for PA0001010 and 05/16/2014 for the purchasing systems.

- In addition, the wholesaler must consult with the Primacy Agency within 30 days to develop an action plan, which it does.  As a result of the consultation occurring on 06/2/2014, a plan is determined that requires the wholesaler no longer use the two wells found with FI+ results within 30 days (by 07/01/2014) and must use water from its other wells to supplement the flow to all the consecutive systems.

- The wholesaler does not meet this schedule but continues to operate the two wells without treatment.

- PWS PA0001010 returns to compliance on 10/01/2014.

The Primacy Agency must report the public notice received from both the wholesale and purchasing systems as outlined in Example #26 using the Enforcement object and associated data elements and values.

The wholesaler PWS has incurred two violations of the treatment technique requirements of the GWR for failing to address contamination on the Primacy Agency directed corrective action schedule resulting from contamination of ground water sources.  The Primacy Agency must report these violations (Exhibits 14 Ex 6-A and 15 Ex 6-B) to EPA, using the Violation object and associated data elements and values.  The Compliance Period Begin Date is 07/2/2014 (the day after the water system should have installed treatment).   Each violation will be associated to the appropriate underlying Corrective Action.  The unique IDs for the contamination corrective actions, which were reported earlier by the primacy agency using the Event Schedule Activity object, are 930 and 931. These must be reported as the Underlying Object ID with the Underlying Data Type set to CORACTION for the respective sources. These are open-ended violations and therefore, the Compliance Period End Date is not reported.  The PWS returns to compliance on 10/01/2014 and the Primacy Agency must report return to compliance enforcement actions (Exhibits 16 Ex 6-C and 17 Ex 6-D) using the Enforcement object and associated data elements and values.

| Exhibit 14 Ex 6-A: Failure to Address Contamination Violation Object Elements |
| --- |
| PWS ID | PA0001010 |
| Facility ID | Do Not Report |
| Violation ID | 13592468 |
| Violation Type Code | 48 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2014-07-02 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 930 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

| Exhibit 15 Ex 6-B: Failure to Address Contamination Violation Object Elements |
| --- |
| PWS ID | PA0001010 |
| Facility ID | Do Not Report |
| Violation ID | 13592469 |
| Violation Type Code | 48 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2014-07-02 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 931 |
| Underlying Data Type | CORACTION |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 16 Ex 6-C: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 98594558 |
| Enforcement Date | 2014-10-01 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 13592468 |

| Exhibit 17 Ex 6-D: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 98594559 |
| Enforcement Date | 2014-10-01 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 13592469 |

### Example #7 - Failure to Conduct Required Source Water Assessment Monitoring

Failure to conduct source water monitoring for assessment purposes

CFR §141.402(a) (1), 141.402(a) (3) and 141.402(b)

Violation Type = 19- Monitoring, GWR Assessment Source Water

Contaminant Code =3002-Enterococcus

Staying with the Example #13 situation but in addition:

- The PWS is required by the Primacy Agency to conduct monthly Assessment Source Water Monitoring (141.402(b)) at each of the four wells, starting August 2013, analyzing the samples for Enterococci.

- The PWS fails to take the required monthly samples at three of the four wells in February 2014.

PA5402427 incurs a Monitoring and Reporting violation for failure to take the Assessment Source Water samples at three of the four wells required.  The Primacy Agency must report this violation (Exhibit 18 Ex 7) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin and End Dates, the first day and last day of the period when monitoring was to be conducted with period defined by the Primacy Agency. Compliance Period End Date is not reported.  The violation requires the Primacy Agency compute if this is a major or minor violation and report the Major Violation Indicator.  A major violation is defined where none of the required samples were collected, analyzed, etc., while a minor is that some, but not all were taken, analyzed, etc.  This is considered a minor violation since the PWS took samples at one of the four wells.

| Exhibit 18 Ex 7: Failure to Conduct Assessment Source Water Monitoring |
| --- |
| PWS ID | PA5402427 |
| Facility ID | Do Not Report |
| Violation ID | 426440 |
| Violation Type Code | 19 |
| Contaminant Code | 3002 |
| Compliance Period Begin Date | 2014-03-01 |
| Compliance Period End Date | 2014-03-31 |
| Analysis Result | Do Not Report |
| Major Violation Indicator | N |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

### Example #8 - Failure To Conduct Continuous Residual Disinfectant Monitoring And Failure To Take Grab Samples At GWR Treatment Plant Serving >3,300 People

Failure to conduct or report compliance monitoring (with 4-log treatment of viruses systems)

CFR §141.403(b)

Violation Type = 31- Monitoring of Treatment (SWTR-Unfilt/GWR)

Contaminant Code = 0700-GWR

PWS PA1327350 is a non-community GWS serving 3,900 people.

- The system has two wells in use year-round and notifies the Primacy Agency in January 2009 that it provides 4-log treatment of viruses before the first customer, using chemical disinfection.

- The system is conducting continuous residual disinfectant monitoring in accordance with CFR § 141.403(b) (3) (i) (A), recording the lowest residual disinfectant concentration every day it serves water to the public.

- For one week that the system is in operation in April 2010, the system fails to conduct continuous residual disinfectant monitoring and does not take grab samples.

- The Primacy Agency notifies the system that it is in violation of the GWR monitoring requirements on 05/25/2010.

PA1327350 is in violation of the GWR for failure to conduct continuous disinfectant monitoring when it has 4-log treatment of viruses in place while providing water to the public.  The Primacy Agency must report this violation (Exhibit 19 Ex 8) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin and End Dates are the first and last days of the month of April 2010.  The violation requires the Primacy Agency compute whether this is a major or minor violation based on the following formula where at least one of the samples was missed/incorrect/etc.:

- Major = fewer than 90% of the samples collected

- Minor = 90 % or more, but not 100% of samples collected

The PWS has been performing continuous residual disinfectant monitoring, and missed a full week of sampling, roughly 25% of samples not taken.  This is a major Monitoring and Reporting violation.

| Exhibit 19 Ex 8: A System Fails to Conduct Compliance Monitoring |
| --- |
| PWS ID | PA1327350 |
| Facility ID | Do Not Report |
| Violation ID | 283327350383 |
| Violation Type Code | 31 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2010-04-01 |
| Compliance Period End Date | 2010-04-30 |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Y |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

### Example #9 - Failure To Conduct Continuous Residual Disinfectant Monitoring But Grab Samples Collected At GWR Treatment Plant Serving >3,300 People

Failure to conduct or report compliance monitoring (with 4-log treatment of viruses systems)

CFR §141.403(b)

Violation Type = 31- Monitoring of Treatment (SWTR-Unfilt/GWR)

Contaminant Code = 0700-GWR

Earlier Example #8 is extended as follows:

- The PWS becomes aware of a malfunction in the continuous monitoring equipment within 1 hour of the failure.

- The PWS resorts to taking grab samples every 4 hours at that location for the five days it takes to restore the continuous monitoring equipment.

- In accordance with 141.403(b)(3)(i)(A), this is an allowable situation, and therefore, there is no violation to be reported to EPA, as long as the PWS restores continuous monitoring equipment within 14 days of the failure.

### Example #10 - PWS without Disinfection Treatment Experiences TCR Total Coliform-Positive Result, Assessment Source Water Monitoring (In Compliance with GWR)

PWS PA5426440 is a community water system serving 3,000 people year round.

- The system has four wells spread out over a large area.  There is no disinfection treatment on any of the wells, and therefore no 4-log treatment of viruses.

- In July 2013, TCR sampling results show a Total Coliform-positive (TC+) result.

- Within 24 hours of being notified of the TC+, the PWS collects the required triggered source water samples for the required fecal indicator at each of the four wells and finds a fecal indicator-positive at two of the wells.

- Upon being notified of the two FI+ results, the PWS immediately consults with the Primacy Agency about a corrective action plan.

- The Primacy Agency instructs the PWS to take five additional source water samples at each of the two wells that had the FI+ results, within 24 hours.

- The PWS complies, and none of these samples is FI+.

- The Primacy Agency directs the PWS to conduct monthly Assessment Source Water Monitoring (CFR §141.402(b)) for Enterococci at each of the four wells over the next 12 months, to obtain a better understanding of the quality of the source water prior to determining a corrective action plan.

- The PWS conducts the Assessment Source Water Monitoring.

The PWS continues to be in compliance with provisions of the GWR

### Example #11 - Failure to Monitor for Additional Source Water Samples

Failure to take a additional samples required by Primacy Agency in response to positive fecal indicator (FI+) assessment sample.

CFR §141.402(b)

Violation Type = 34- Monitoring, GWR Triggered/Additional

Contaminant Code = 3014-E. coli

PWS PA1208154 is a non-community GWS serving 44,000 people.

- The primacy agency requires its PWS to use E. coli as the fecal indicator for GWR.

- The system has ten wells in use year-round and does not provide 4-log treatment of viruses before the first customer.

- The PWS is notified of a positive fecal indicator (FI+) triggered source water sample on 08/19/2010 at one of the wells.

- Within 24 hours of notification of the FI+ sample result, the PWS must provide public notice and per the Primacy Agency’s direction take five additional samples.

- The system provides public notice; however, it does not collect any additional samples.

PWS PA1208154 is in violation of the GWR for failure to take the required additional source water monitoring samples within 24-hours of a FI+.   The Primacy Agency must report this violation (Exhibit 20 Ex 11-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 08/21/2010, the first day after the monitoring was to be conducted. This is an open-ended violation and therefore the Compliance Period End Date is not reported.  This is a Monitoring and Reporting violation that also requires the Primacy Agency to identify whether it’s a major or minor violation. A major violation is defined where none of the required samples were collected, analyzed, etc, while a minor is that some, but not all were taken, analyzed, etc. In this example, none of the samples were taken; therefore, this is a major violation.   The unique ID for the precipitating sample result, 653905214, must be reported as the Underlying Object ID with the Underlying Data Type set to SMPLRESULT for this   violation.  The PWS returned to compliance on 09/06/2010 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 21 Ex 11-B) using the Enforcement object and associated data elements and values.

| Exhibit 20 Ex 11-A: Failure to Conduct Additional Source Water Monitoring |
| --- |
| PWS ID | PA1208154 |
| Facility ID | Do Not Report |
| Violation ID | 18716 |
| Violation Type Code | 34 |
| Contaminant Code | 3014 |
| Compliance Period Begin Date | 2010-8-21 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Y |
| Underlying Object ID | 653905214 |
| Underlying Data Type | SMPLRESULT |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 21 Ex 11-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA1208154 |
| Enforcement ID | 98594419 |
| Enforcement Date | 2010-09-06 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 18716 |

The Primacy Agency must report the public notice received from system as outlined in Example #26 using the Enforcement object and associated data elements and values.

### Example #12 - PWS with Disinfection Treatment Experiences TCR Routine, Total Coliform-Positive, Result

Failure to conduct triggered source water monitoring –

CFR §141.402(a) (1)

Violation Type = 34- Monitoring, GWR Triggered/Additional

Contaminant Code = 0700-GWR

This example uses the same situation as Example #10, except the PWS does have 4-log treatment of viruses in place and the system is in compliance with Section 141.403(b) which requires a PWS with 4-log treatment of viruses to monitor the effectiveness and reliability of the treatment.

Under these circumstances, triggered source water monitoring is not required in response to a positive TCR routine sample and there is no violation. However, the PWS must continue compliance monitoring.

### Example #13 - PWS without Disinfection Treatment Experiences TCR Total Coliform-Positive Result and Fails to Conduct Triggered Source Water Monitoring

Failure to conduct triggered source water monitoring –

##### CFR §141.402(a) (1)

Violation Type = 34- Monitoring, GWR Triggered/Additional

Contaminant Code = 3028-Coliphage

PWS PA5402427 is a community GWS serving 10,000 people.

- The primacy agency requires its PWS to use coliphage as the fecal indicator for GWR.

- The system has four wells in use year-round and does not provide 4-log treatment of viruses before or at the first customer.

- On 12/15/2011, the system is notified by the laboratory that one of its routine TCR samples collected on 12/12/2011 is total-coliform-positive (TC+).

- The system collects three repeat samples as required under the TCR, but does not collect any of the required triggered source water samples.

- Several conditions exist where the Primacy Agency may waive a PWS’s need to conduct triggered source water monitoring (e.g., TC+ sample invalidated, documentation that TC+ results from distribution system deficiency); but  Primacy Agency has determined that none of these applies.

PA5402427 is in violation of the GWR for failure to take the required triggered source water monitoring within 24-hours of notification of TCR routine TC+.  The Primacy Agency must report this violation (Exhibit 22 Ex 13-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 12/17/2011, the first day after the monitoring was to be conducted.  This is an open-ended violation and therefore the Compliance Period End Date is not reported. This is a Monitoring and Reporting violation that also requires the Primacy Agency to identify whether it’s a major or minor violation.  A major violation is defined where none of the required samples were collected, analyzed, etc, while a minor is that some, but not all were taken, analyzed, etc. In this example, none of the samples were taken; therefore, this is a major violation.  The unique ID for the precipitating sample result, 54289W-2, must be reported as the Underlying Object ID with the Underlying Data Type set to SMPLRESULT for this violation.  The PWS returned to compliance on 12/28/2011 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 23 Ex 13-B) using the Enforcement object and associated data elements and values.

| Exhibit 22 Ex 13-A: Failure to Conduct Triggered Source Water Monitoring |
| --- |
| PWS ID | PA5402427 |
| Facility ID | Do Not Report |
| Violation ID | 427454402 |
| Violation Type Code | 34 |
| Contaminant Code | 3028 |
| Compliance Period Begin Date | 2011-12-17 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Y |
| Underlying Object ID | 54289W-2 |
| Underlying Data Type | SMPLRESULT |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 23 Ex 13-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA5402427 |
| Enforcement ID | 98594489 |
| Enforcement Date | 2011-12-28 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 427454402 |

### Example #14 - Failure to Take Required Complete Set of Triggered Source Water Monitoring Samples

Failure to conduct triggered source water monitoring.

##### CFR §141.402(a) (1), CFR §141.402(a) (3) and CFR §141.402(b)

Violation Type = 34- Monitoring, GWR Triggered/Additional

Contaminant Code = 3002-Enterococcus

PWS PA5002427 is a non-community GWS serving 1,200 people with two interconnected distribution systems and is required to take two samples each quarter for TCR.

- The primacy agency requires its PWS to use enterococcus as the fecal indicator for GWR.

- The system has four wells in use year-round and does not provide 4-log treatment of viruses before or at the first customer.

- On 05/03/2012, the system is notified by the laboratory that two of its routine quarterly total coliform samples collected on 04/30/2012 are total-coliform-positive (TC+).  The unique identifiers In the Primacy Agency’s database for these two sample results are 2012-8350142 and 2012-8350143.

- Under the TCR, the water system must collect two sets of three distribution system total coliform samples; under the GWR, it must collect two sets of four triggered source water samples.

- The system collects two sets of repeat samples as required by TCR, but collects only one of the four GWR-required triggered source water samples for the first TC+ result and none of the four required triggered source water samples for the second TC+ result.

PA5402427 is in violation of the GWR for failure to take the required a complete set of triggered source water monitoring samples at each source for each TCR routine TC+ distribution sample. The Primacy Agency must report these violations (Exhibits 24 Ex 14-A and 25 Ex 14-B) to EPA using the Violation object with the following data elements and values. The Compliance Period Begin Date is 05/05/2012, the first day after the monitoring was to be conducted.  These are open-ended violations and therefore the Compliance Period End Date is not reported. This is a Monitoring and Reporting violation that also requires the Primacy Agency to identify whether it’s a major or minor violation.  A major violation is defined where none of the required samples were collected, analyzed, etc, while a minor is that some, but not all were taken, analyzed, etc.

Only one of the four samples was taken in response to the first precipitating TC+ sample result 2012-8350142; therefore, this is a minor violation (Exhibit 24 Ex 14-A).   The unique ID for the sample result must be reported as the Underlying Object IDs with the Underlying Date Type set to SMPLRESULT.

No samples were taken in response to precipitating TC+ sample result 2012-8350143; therefore, this is a major violation (Exhibit 25 Ex 14-B).  The unique ID for the sample result must be reported as the Underlying Object IDs with the Underlying Date Type set to SMPLRESULT.   The PWS returned to compliance on 05/23/2012 and the Primacy Agency must report a return to compliance enforcement actions (Exhibits 26 Ex 14-C and 27 Ex 14-D) using the Enforcement object and associated data elements and values.

| Exhibit 24 Ex 14-A: Failure to Conduct Triggered Source Water Monitoring |
| --- |
| PWS ID | PA5002427 |
| Facility ID | Do Not Report |
| Violation ID | 427453302 |
| Violation Type Code | 34 |
| Contaminant Code | 3002 |
| Compliance Period Begin Date | 2012-05-05 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | N |
| Underlying Object ID | 2012-8350142 |
| Underlying Data Type | SAMPRESULT |
| Severity Indicator Count | Do Not Report |

| Exhibit 25 Ex 14-B: Failure to Conduct Triggered Source Water Monitoring |
| --- |
| PWS ID | PA5002427 |
| Facility ID | Do Not Report |
| Violation ID | 427453303 |
| Violation Type Code | 34 |
| Contaminant Code | 3002 |
| Compliance Period Begin Date | 2012-05-05 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Y |
| Underlying Object ID | 2012-8350143 |
| Underlying Data Type | SAMPRESULT |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 26 Ex 14-C: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA5002427 |
| Enforcement ID | 98595589 |
| Enforcement Date | 2012-05-23 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 427453302 |

| Exhibit 27 Ex 14-D: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA5002427 |
| Enforcement ID | 98595590 |
| Enforcement Date | 2012-05-23 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 427453303 |

### Example #15 - Failure to Notify Primacy Agency of Failure to Maintain Minimum Disinfection

Failure to notify Primacy Agency that the system fails to meet the Primacy Agency specified compliance monitoring requirements.

CFR §141.405(a)(1)

Violation Type = 05- Notification, State

Contaminant Code = 0700-GWR

PWS PA1234567 is a community GWS serving 8,500 people as outlined in Example #1 and #2.

- The system has two wells in use year-round and notifies the Primacy Agency in March 2009 that it provides 4-log treatment of viruses before the first customer.

- On 01/22/2011 (a Saturday), the chlorine residual at the entry point drops below the required level set by the Primacy Agency.  The operator determines that due to a malfunctioning chlorine pump, the system has not been providing 4-log treatment of viruses at one of its wells.

- The PWS operator corrects the malfunctioning chlorine pump by the end of the week following the initial drop in chlorine residual, i.e., by 1/28/2011.

- The system officially notifies the Primacy Agency of its failure to consistently provide 4-log treatment of viruses with its monthly operating report to the Primacy Agency on 02/01/2011.

- The PWS returns to compliance on 07/30/2011.

The PWS has incurred two violations. The first is the failure to maintain the required minimum disinfectant residual in the distribution system every day. See Example #2  for information on how to report it.

The second violation is a violation of the Primacy Agency notification requirements of GWR for failing to notify the Primacy Agency by the next business day of the failure to maintain the required minimum residual disinfectant every day. The Primacy Agency must report this violation (Exhibit 28 Ex 15-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 01/25/2011 (one day after the PWS must notify the Primacy Agency). This is an open-ended violation and therefore, the Compliance Period End Date is not reported. The PWS returns to compliance on 07/30/2015 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 29 Ex 15-B) using the Enforcement object and associated data elements and values.

| Exhibit 28 Ex 15-A: Failure to Notify Primacy Agency of Compliance Monitoring Exceedance |
| --- |
| PWS ID | PA1234567 |
| Facility ID | Do Not Report |
| Violation ID | 2468936 |
| Violation Type Code | 05 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2011-01-25 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 29 Ex 15-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA1234567 |
| Enforcement ID | 5042 |
| Enforcement Date | 2011-07-30 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 2468936 |

### Example #16 - Failure to Notify Primacy Agency of Completion of Corrective Action

Failure to notify Primacy Agency a distribution system total coliform sample meets the triggered source water monitoring exception criteria.

CFR §141.402(a)(5), CFR § 141.405(a)(3)

Violation Type = 05- Notification, State

Contaminant Code = 0700-GWR

This example uses the same situation as in Example #4, except the PWS does not notify the Primacy Agency when the corrective action is completed.  The PWS returns to compliance on 04/30/2015.

The PWS has incurred a violation of the Primacy Agency notification requirements of the GWR for failing to notify the Primacy Agency within 30 days of completion of a corrective action.  The Primacy Agency must report this violation (Exhibit 30 Ex 16-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 03/28/2015 (one day after the PWS must notify the Primacy Agency).  This is an open-ended violation and therefore, the Compliance Period End Date is not reported.   The PWS returns to compliance on 04/30/2015 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 31 Ex 16-B) using the Enforcement object and associated data elements and values.

| Exhibit 30 Ex 16-A: Failure to Notify Primacy Agency of Completed Corrective Action |
| --- |
| PWS ID | PA2154776 |
| Facility ID | Do Not Report |
| Violation ID | 2468361 |
| Violation Type Code | 05 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2015-03-28 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 31 Ex 16-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA2154776 |
| Enforcement ID | 88951 |
| Enforcement Date | 2015-04-30 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 2468361 |

### Example # 17 - Failure to Notify Primacy Agency of Exception to Triggered Source Water Monitoring

Failure to notify Primacy Agency a distribution system total coliform sample meets the triggered source water monitoring exception criteria.

CFR §141.402(a)(5), CFR § 141.405(a)(3)

Violation Type = 05- Notification, State

Contaminant Code = 0700-GWR

This example uses the same situation as in Example #13 , except that the PWS indicates the TC+ resulted from a distribution system deficiency.

PWS PA5402427 is a community GWS serving 10,000 people.

- The primacy agency requires its PWS to use coliphage as the fecal indicator for GWR.

- The system has four wells in use year-round and does not provide 4-log treatment of viruses before or at the first customer.

- On 12/15/2011, the system is notified by the laboratory that one of its routine TCR samples collected on 12/12/2011 is total-coliform-positive (TC+).

- The system collects three repeat samples as required under the TCR, but does not collect any of the required triggered source water samples.

- CFR §Section 141.402(a)(5) allows for two exceptions to triggered source water monitoring, both of which are associated with confirming or documenting that the TC+ sample results from distribution system deficiencies.

- Under CFR §141.402(a)(5)(i), the Primacy Agency must document in writing that the TC+ resulted from a distribution system deficiency, or under CFR §141.402(a)(5)(ii), that the total coliform-positive sample collected under CFR § 141.21(a) is collected at a location that meets Primacy Agency criteria for distribution system conditions that will cause total coliform-positive samples.

- If one of these conditions is met, then the PWS need not perform triggered source water monitoring, and there is no violation to be reported to EPA.

- The PWS returns to compliance on 07/30/2015.

- In accordance with Section 141.402(a) (5)(ii), the PWS does not need to conduct triggered source water monitoring; however, in accordance with Section 141.405(a)(3), it must notify the Primacy Agency in writing within 30 days of receiving notification of the positive sample result.

- In this example, the PWS does not notify the Primacy Agency in writing that the TC+ result from TCR monitoring is caused by distribution system deficiencies.

The PWS has incurred a violation of the Primacy Agency notification requirements of the GWR for failing to notify the Primacy Agency within 30 days of receiving notification of the distribution system total coliform sample.  The Primacy Agency must report this violation (Exhibit 32 Ex 17-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 07/20/2015 (one day after the PWS must notify the Primacy Agency).  This is an open-ended violation and therefore, the Compliance Period End Date is not reported.   The PWS returns to compliance on 07/30/2015 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 33 Ex 17-B) using the Enforcement object and associated data elements and values.

| Exhibit 32 Ex 17-A: Failure to Notify Primacy Agency of Triggered Source Water Monitoring Exception Criteria |
| --- |
| PWS ID | PA5402427 |
| Facility ID | Do Not Report |
| Violation ID | 2468999 |
| Violation Type Code | 05 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2015-07-20 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 33 Ex 17-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA5402427 |
| Enforcement ID | 88937 |
| Enforcement Date | 2015-07-30 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 2468999 |

### Example #18 - Failure to Maintain Records

Failure to maintain records of compliance monitoring.

CFR §141.405(b)

Violation Type = 09-Record Keeping

Contaminant Code = 0700-GWR

PWS PA3289302 is a community water system serving 15,000 people.

- The system uses surface, ground water under the direct influence of surface water (GWUDI) and ground water to supply the community.

- The surface/GWUDI and ground water sources are not mixed, supplying distinctly different portions of the distribution system.

- 4-log treatment of viruses using chemical disinfection is performed on the ground water sources.

- The PWS conducts continuous compliance monitoring of residual disinfectant at the appropriate sampling sites.

- On 2/15/2012, the Primacy Agency performs a sanitary survey on the PWS and discovers that the system has not maintained records of the compliance monitoring from 07/01/2011 until 01/01/2012.

- The PWS returns to compliance on 01/01/2013.

The Primacy Agency must report this violation (Exhibit 33 Ex 18-A) to EPA using the Violation object with the following data elements and values. The Compliance Period Begin Date is 07/01/2011 (the date the PWS failed to maintain records). This is an open-ended violation and therefore, the Compliance Period End Date is not reported. The PWS returns to compliance on 1/1/2013 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 35 Ex 18-B) using the Enforcement object and associated data elements and values.

| Exhibit 34 Ex 18-A: Failure to Address a Deficiency Violation Object Elements |
| --- |
| PWS ID | PA3289302 |
| Facility ID | Do Not Report |
| Violation ID | 347302299 |
| Violation Type Code | 09 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2011-07-01 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 35 Ex 18-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA3289302 |
| Enforcement ID | 34828023089 |
| Enforcement Date | 2013-01-01 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 347302299 |

### Example #19 - Failure to Consult Regarding a Significant Deficiency

Failure to consult with Primacy Agency regarding significant deficiency.

CFR §141.403(a)(4)

Violation Type = 20-Failure to Respond/Consult with State

Contaminant Code = 0700-GWR

This example uses the same situation as in Example #18, except PWS does not consult with the Primacy Agency regarding the significant deficiency.

PWS PA3289302 is a community water system serving 15,000 people.

- The system utilizes surface, ground water under the direct influence of surface water (GWUDI) and ground water to supply the community.

- The surface/GWUDI and ground water sources are not mixed, supplying distinctly different portions of the distribution system.

- 4-log treatment of viruses using chemical disinfection is performed on the ground water sources.

- The PWS conducts continuous compliance monitoring of residual disinfectant at the appropriate sampling sites.

- On 2/15/2012, the Primacy Agency performs a sanitary survey on the PWS and finds a significant deficiency in a portion of the distribution system served solely by the ground water sources, providing notification of the findings on 2/18/2012.

- The PWS fails to consult with the State regarding the appropriate corrective actions within 30 days of receiving the notice of the significant deficiency or 03/19/2012.

- The Primacy Agency does not identify a specific corrective action plan, and the PWS consults with the State on 05/10/2012 regarding an appropriate corrective action plan.

- The PWS returns to compliance on 05/10/2012

The PWS is subject to the treatment technique provisions of Section 141.403 because of the significant deficiency found in the portion of the distribution system served solely by ground water. As a result, the PWS is in violation of treatment technique requirements beginning the day after the consultation should have occurred.

The Primacy Agency must report this violation (Exhibit 36 Ex 19-A) to EPA using the Violation object with the following data elements and values. The Compliance Period Begin Date is 03/20/2012 (one date after the PWS was to consult with the Primacy Agency). A single failure to consult violation is issued regardless of the number of significant deficiencies or contaminated source water facilities. This is an open-ended violation and therefore, the Compliance Period End Date is not reported. The PWS returns to compliance on 05/10/2012 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 37 Ex 19-B) using the Enforcement object and associated data elements and values.

| Exhibit 36 Ex 19-A: Failure to Consult Regarding a Deficiency Violation Object Elements |
| --- |
| PWS ID | PA3289302 |
| Facility ID | Do Not Report |
| Violation ID | 347302289 |
| Violation Type Code | 20 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2012-03-20 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 37 Ex 19-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA3289302 |
| Enforcement ID | 34828023089 |
| Enforcement Date | 2012-05-10 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 347302289 |

### Example #20 - Failure to Consult with Primacy Agency Multiple Deficiencies

Failure to consult with Primacy Agency in response to multiple sanitary survey deficiencies within 30 days.

CFR §141.404(a)

Violation Type = 20-Failure to Respond/Consult with State

Contaminant Code = 0700-GWR

This example uses the situation in Example #5 , except the PWS does not consult with the Primacy Agency regarding the significant deficiencies.

PWS PA1093487 is a community GWS serving 1,500 people.

- The system has one well in use year-round.

- During a sanitary survey on 06/01/2013, the Primacy Agency identifies two significant deficiencies—the chlorination room is not explosion proof and lacks any safety equipment and the well casing does not extend above the ground surface.

- The system is notified of the deficiencies on 06/10/2013 in a letter from the Primacy Agency.

- The PWS fails to contact the Primacy Agency within 30 days of receiving written notice (07/10/2013) of the significant deficiencies.

- The Primacy Agency, in following up on this problem, submits a letter to the PWS on 07/18/2013, detailing the violation and reminding them to address the deficiencies by 10/08/2013.

The PWS was negligent in not contacting the Primacy Agency within 30 days of receipt of written notification of a significant deficiency.  The PWS is in violation of Section 141.403(a) (4).  The Primacy Agency must report this violation (Exhibit 38 Ex 20-A) to EPA using the Violation object with the following data elements and values.  Even though there were multiple significant deficiencies to address, there was only one need to consult and therefore only one violation will be reported.  The Compliance Period Begin Date is 07/11/2013 (one day after the PWS was to consult).  This is an open-ended violation and therefore, the Compliance Period End Date is not reported.   The PWS returned to compliance on 08/04/2013 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 39 Ex 20-B) using the Enforcement object and associated data elements and values.

| Exhibit 38 Ex 20-A: Failure to Consult Regarding Multiple Deficiencies Violation Object Elements |
| --- |
| PWS ID | PA7654321 |
| Facility ID | Do Not Report |
| Violation ID | 27474712 |
| Violation Type Code | 20 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2013-07-11 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 39 Ex 20-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA7654321 |
| Enforcement ID | 34828023089 |
| Enforcement Date | 2013-08-04 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 27474712 |

### Example #21 - Failure to Consult Contamination

Failure to take a consult with the State in response to a fecal indicator positive source water sample result within 30 days.

CFR §141.403(a)(4)

Violation Type = 20- Failure to Respond/Consult with State

Contaminant Code = 0700-GWR

This example uses the situation in Example #6, except wholesaler PWS PA0001010 fails to consult with the Primacy Agency regarding the fecal indicator contamination.

Wholesaler PWS PA0001010 has 15 wells providing ground water to seven different purchasing PWSs.  PWS PA7654321 serves 5,000 people purchasing all its raw untreated water from PWS PA0001010.

- As part of its routine TCR sampling, PA7654321 is notified by its laboratory of a Total Coliform-positive (TC+) sample taken on 05/12/2014.

- In accordance with Section 141.402(a) (4), PA7654321 notifies its wholesaler, PA0001010, within 24 hours of having a TC+.

- Wholesaler PA0001010 must perform triggered source water monitoring within 24 hours of receipt of the notice from PA7654321.

- PA0001010 performs required triggered source water monitoring and is notified by its laboratory on 05/14/2014 of a fecal indicator-positive (FI+) result on two of its wells, Northside #1 and Northside #2.

- The wholesaler must notify all the consecutive systems served by these sources of the FI+ result, which it does on 05/15/2014.  The wholesaler and seven purchasing systems must all provide public notice within 24 hours of notification, which is 05/15/2014 for PA0001010 and 05/16/2014 for the purchasing systems.

- The PWS fails to contact the Primacy Agency within 30 days of receiving written notice (06/15/2014) of the fecal indicator-positive (FI+) sample result.

The PWS was negligent in not contacting the Primacy Agency within 30 days of receipt of written notification of a fecal indicator positive source water sample.  The PWS is in violation of Section 141.403(a) (4).  The Primacy Agency must report this violation (Exhibit 40 Ex 21-A) to EPA using the Violation object with the following data elements and values.  Even though there were multiple source water facilities with contamination to address, there was only one need to consult and therefore only one violation will be reported.  The Compliance Period Begin Date is 06/16/2014 (one day after the PWS was to consult).  This is an open-ended violation and therefore, the Compliance Period End Date is not reported.   The PWS returned to compliance on 08/04/2014 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 41 Ex 21-B) using the Enforcement object and associated data elements and values.

| Exhibit 40 Ex 21-A: Failure to Consult Regarding Fecal Contamination Violation Object Elements |
| --- |
| PWS ID | PA0001010 |
| Facility ID | Do Not Report |
| Violation ID | 7XX4791 |
| Violation Type Code | 20 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2014-06-16 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 41 Ex 21-B: Enforcement Action Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 34828023089 |
| Enforcement Date | 2014-08-04 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 7XX4791 |

### Example #22 - Sanitary Survey Cooperation Failure

CFR §141.401(a)

Violation Type = 28-Sanitary Survey Cooperation Failure

Contaminant Code 0700-GWR

PWS PA8426490 is a community water system serving 30,000 people year round.

- The system has four wells spread over a large area.

- On 01/15/2012, the Primacy Agency informs the PWS it will perform a sanitary survey on 2/12/2012, and requests staff be available to provide access to water system facilities and operational records.

- On 02/12/2012, when Primacy Agency staff show up to perform the sanitary survey, the PWS chief operator is on vacation and cannot be reached, and his staff is unwilling or unable to provide access to the operational records and/or facilities.

- The Primacy Agency sanitarian does not perform the sanitary survey.  Upon returning from vacation, the PWS chief operator remembers he neglected to inform his staff of the scheduled survey, and he assembles the operational records and forwards them to the Primacy Agency and reschedules an appointment for the sanitary survey.

- The PWS returns to compliance on 03/05/2012.

PA8426490 is in violation of 141.401(a) that states:

“(a) Ground water systems must provide the Primacy Agency, at the Primacy Agency's request, any existing information that will enable the Primacy Agency to conduct a sanitary survey.”

The violation begins when the PWS’s staff is unwilling/unable to provide access to either the operational records and/or facilities for the survey (02/12/2012).  The Primacy Agency must report this violation (Exhibit 42 Ex 22-A) to EPA using the Violation object with the following data elements and values.  The PWS returns to compliance on 03/05/2012 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 43 Ex 22-B) using the Enforcement object and associated data elements and values.

| Exhibit 42 Ex 22-A: Sanitary Survey Cooperation Failure |
| --- |
| PWS ID | PA8426490 |
| Facility ID | Do Not Report |
| Violation ID | 152902012 |
| Violation Type Code | 28 |
| Contaminant Code | Do Not Report |
| Compliance Period Begin Date | 2012-02-12 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 43 Ex 22-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA8426490 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2012-03-05 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 152902012 |

### Example #23 - Failure to Notify Purchase PWS

Failure by wholesaler to notify purchase water systems when positive source water sample results found

CFR §141.402(a) (4)

Violation Type = 73-Failure To Notify Other PWS

Contaminant Code = 0700-GWR

PWS PA7654321 serves 5,000 people

- The system purchases all its water, which is untreated, from wholesaler PWS PA0001010.

- The wholesaler has 15 wells providing ground water to seven different PWSs.

- As part of its routine TCR sampling, purchasing system PA7654321 is notified by its laboratory of a TCR routine total coliform-positive (TC+) sample taken on 05/12/2014.

- In accordance with Section 141.402(a) (4), the purchasing system must notify its wholesaler within 24 hours of the TCR TC+ sample.

- Wholesaler PA0001010 must perform triggered source water monitoring within 24 hours of receipt of the notice from PA7654321.

- PA0001010 performs the required triggered source water monitoring and is notified by its laboratory on 05/14/2014 of a fecal indicator-positive (FI+) result for two of its wells.

- The wholesaler must notify all the consecutive systems served by these sources of the FI+ result; but it does not make this notification.

- The wholesale system returns to compliance on 06/03/2014.

Wholesaler PA0001010 has incurred a violation of the notification requirements of the GWR for failure to notify consecutive systems of its FI+.  The Primacy Agency must report this violation (Exhibit 44 Ex 23-A) to EPA using the Violation object with the following data elements and values. The Compliance Period Begin Date is 05/16/2014 (the date after not providing the required notification). This is an open-ended violation and therefore, the Compliance Period End Date is not reported.  The PWS returns to compliance on 06/03/2014 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 45 Ex 23-B) using the Enforcement object and associated data elements and values.

| Exhibit 44 Ex 23-A: Failure to Notify Other PWS |
| --- |
| PWS ID | PA0001010 |
| Facility ID | Do Not Report |
| Violation ID | 426420 |
| Violation Type Code | 73 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2014-05-16 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 45 Ex 23-B: Enforcement Object Violation Returned to Compliance for “Open-ended” Violation |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2014-06-03 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 426420 |

### Example #24 - Failure to Notify Wholesale PWS

Failure to notify consecutive system’s wholesaler when positive TCR sample results found

CFR §141.402(a) (4)

Violation Type = 73- Failure To Notify Other PWS

Contaminant Code = 0700-GWR

This example uses the situation in Example #23, except the purchasing system, PA7654321, does not notify the wholesaler about the TCR routine TC+ distribution system sample result. The purchasing system returns to compliance on 06/03/2014.

The purchasing PWS has incurred a violation of the notification requirements of the GWR for failure to notify its wholesaler system of its TC+ sample result.  The Primacy Agency must report this violation (Exhibit 46 Ex 24-A) to EPA using the Violation object with the following data elements and values.  The Compliance Period Begin Date is 05/14/2014 (the date after not providing the required notification). This is an open-ended violation and therefore, the Compliance Period End Date is not reported.  The PWS returns to compliance on 06/03/2014 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 47 Ex 24-B) using the Enforcement object and associated data elements and values.

| Exhibit 46 Ex 24-A: Failure to Notify Other PWS |
| --- |
| PWS ID | PA7654321 |
| Facility ID | Do Not Report |
| Violation ID | 426420 |
| Violation Type Code | 73 |
| Contaminant Code | 0700 |
| Compliance Period Begin Date | 2014-05-14 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 47 Ex 24-B: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA7654321 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2014-06-03 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 426420 |

### Example #25 - Public Notification of Violation

Failure to provide public notification for a violation

CFR §141.202

Violation type = 75- PN Violation for an NPDWR Violation

Contaminant Code = 7500-GWR

This example uses the same situation described in Example #2, but in addition to receiving the violation for failing to maintain treatment, the PWS does not make public notice of that violation.

- PA1234567 is officially notified by the Primacy Agency of its failure to consistently provide 4-log treatment of viruses in a letter from the Primacy Agency on 2/01/2011.

- The letter also notified PA1234567 it must provide public notice to its customers within 30 days of the violation notification, 03/03/2011, and proof of the public notice to the Primacy Agency within 40 days, 03/13/2011.

- PA1234567 did not provide public notification and was notified on 05/12/2011 that since it had not provided public notification, it had incurred a public notification violation.

- Further, PA1234567must provide public notice as soon as possible and submit proof to the Primacy Agency.  The system provided public notification on 05/20/2011 and faxed proof to the Primacy Agency on the same day.

- The PWS returns to compliance on 05/20/2011.

As with any public notification, the Primacy Agency must report the date it requested the public notification from the water system, 02/01/2011, and the date the water system provided the public notification, 05/20/2011 (Exhibits 48 Ex 25-A and 51 Ex 25-D).  These enforcement actions are associated to the "original" failure to provide treatment violation #0100121.

The Primacy Agency must report the public notice violation (Exhibits 49 Ex 25-B) to EPA using the Violation object and associated data elements and values.  Since the public notice was the result of a National Primary Drinking Water Regulation (NPDWR) "original" violation, the violation type is type 75 and, when this violation is reported to EPA, the underlying "original" violation #0100121 is required.  This must be reported as the Underlying Object ID with the Underlying Data Type set to PNORIGVIOL.  The Compliance Period Begin Date is 03/04/2011 (the day after not providing the required notification). This is an open-ended violation and therefore, the Compliance Period End Date is not reported.  The PWS returns to compliance on 05/20/2011 and the Primacy Agency must report a return to compliance enforcement action (Exhibit 50 Ex 25-C) using the Enforcement object and associated data elements and values.

| Exhibit 48 Ex 25-A: Enforcement Object Primacy Agency Request for Public Notice |
| --- |
| PWS ID | PA1234567 |
| Enforcement ID | 34828033 |
| Enforcement Date | 2011-02-01 |
| Action Code | SIE |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 0100121 |

| Exhibit 49 Ex 25-B: Failure to Provide Public Notice |
| --- |
| PWS ID | PA1234567 |
| Facility ID | Do Not Report |
| Violation ID | 426420 |
| Violation Type Code | 75 |
| Contaminant Code | 7500 |
| Compliance Period Begin Date | 2011-03-03 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Underlying Object ID | 0100121 |
| Underlying Data Type | PNORIGVIOL |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 50 Ex 25-C: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA1234567 |
| Enforcement ID | 34828123 |
| Enforcement Date | 2011-05-20 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 426420 |

| Exhibit 51 Ex 25-D: Enforcement Object Water System Provides Public Notice |
| --- |
| PWS ID | PA1234567 |
| Enforcement ID | 34828124 |
| Enforcement Date | 2011-05-20 |
| Action Code | SIF |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 0100121 |

### Example #26 - Public Notice Requested and Received

Provide Public Notice for fecal indicator positive source water sample.

CFR §141.402(g)

- This example is based on earlier Example #6, where wholesaler PWS PA0001010 performed required triggered source water monitoring and was notified by its laboratory on 05/14/2014 of a fecal indicator-positive (FI+) result on two of its wells.

- The wholesaler notified all the consecutive systems served by these sources of the FI+ result within 24 hours of learning of the positive triggered source water sample as required.

- The wholesaler and all seven purchase systems all provided public notice within 24 hours (i.e., by 05/15/2015 for the wholesale system and 05/16/2014 for the purchase systems) as required.

The Primacy Agency must report the public notice received from both the wholesale and purchasing systems using the Enforcement object and associated data elements and values.  Exhibits 52 Ex 26-A and Exhibit 53 Ex 26-B outline the reporting for the wholesale system.  Similar reporting must be submitted for each of the seven purchase systems.

| Exhibit 52 Ex 26-A: Enforcement Action Object Public Notice Received for Wholesale System |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 98594559 |
| Enforcement Date | 2014-5-15 |
| Action Code | SIF |
| Enforcement Comment | Optional |
| Associated Violation ID(s) |  |

| Exhibit 53 Ex 26-B: Enforcement Action Object Public Notice Received for Purchase System |
| --- |
| PWS ID | PA7654321 |
| Enforcement ID | 98594560 |
| Enforcement Date | 2014-5-16 |
| Action Code | SIF |
| Enforcement Comment | Optional |
| Associated Violation ID(s) |  |

### Example #27 - Public Notification of Positive Source Water

Failure to provide public notification for a fecal-indicator positive sample

CFR §141.402(g)

Violation Type = 76- PN Violation without NPDWR Violation

Contaminant Code = 7500-PNR

This example continues Example #26 with the following exceptions:

- Though wholesaler PA0001010 both notified its purchasing systems about the positive sample and provided notification to its own customers of the fecal-indicator positive triggered source sample, it did not do either notification within the required 24 hours of receiving the notification of the FI+ result from the laboratory, which was received on 05/14/2014.

- During a 06/2/2014 consultation, the Primacy Agency notified PA0001010 that public notification should have been provided to its direct customers on 05/15/2014 and requested it notify its direct customers as soon as possible.

- PA0001010 notifies its consecutive systems on 06/03/2014.  However, the PWS must have notified the consecutive systems within 24 hours of receiving the 05/14/2014 FI+ notification from its laboratory.

As with any public notification the Primacy Agency must report the date it requested the public notification from the water system and the date the water system provided the public notification, 06/03/2014 (Exhibits 54 Ex 27-Aand 55 Ex 27-B).  These enforcement actions are not associated to a violation as they are not the result of a violation but rather a FI+ sample.

Wholesaler PA0001010 has incurred a violation of the notification requirements of the GWR for failing to notify directly to consumers of its FI+.  The Primacy Agency must report this violation (Exhibit 56 Ex 27-C) to EPA using the Violation object with the following data elements and values.  Since there is not an underlying federal violation the violation type is 76 and the Underlying Object ID and Underlying Data Type are not reported.  The Compliance Period Begin Date is 05/16/2014 (the date after the required notification was due.)  This is an open-ended violation and therefore, the Compliance Period End Date is not reported.  The PWS is back in compliance on 06/03/2014.  The Primacy Agency must report a return to compliance enforcement action (Exhibit 57 Ex 27-D) using the Enforcement object and associated data elements and values.

| Exhibit 54 Ex 27-A: Enforcement Object Primacy Agency Request for Public Notice |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2014-06-02 |
| Action Code | SIE |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | Do Not Report |

| Exhibit 55 Ex 27-B: Enforcement Object Water System Provides Public Notice |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2014-06-03 |
| Action Code | SIF |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | Do Not Report |

| Exhibit 56 Ex 27-C: PN Violation without NPDWR Violation |
| --- |
| PWS ID | PA0001010 |
| Facility ID | Do Not Report |
| Violation ID | 426419 |
| Violation Type Code | 76 |
| Contaminant Code | 7500 |
| Compliance Period Begin Date | 2014-05-16 |
| Compliance Period End Date | Do Not Report* |
| Analysis Result | Do Not Report |
| Major Violation Indicator | Do Not Report |
| Original Violation | Do Not Report |
| Underlying Object ID | Do Not Report |
| Underlying Data Type | Do Not Report |
| Severity Indicator Count | Do Not Report |

* These are defined as “open-ended” violations. For these, primacy agencies must not report a Compliance Period End Date as part of the violation transaction. Instead, to close one of these violations, primacy agencies must report either: (1) when the water system has met the “returned to compliance (RTC)” criteria; or (2) when the rule no longer applies; or (3) when the water system became inactive. To report that the violation is RTC, report an enforcement transaction with the code value of SOX/EOX along with the date, and a link to the violation. To report that the rule no longer applies to the PWS, report an enforcement transaction with code values of SO0/EO0 along with the date and a link to the violation. SDWIS/Data Warehouse processing will then populate the Compliance Period End Date field with the date contained in the enforcement action transaction or the water system inactivation date.

| Exhibit 57 Ex 27-D: Enforcement Object Violation Returned to Compliance for “Open-Ended” Violation |
| --- |
| PWS ID | PA0001010 |
| Enforcement ID | 34828022 |
| Enforcement Date | 2014-06-03 |
| Action Code | SOX |
| Enforcement Comment | Optional |
| Associated Violation ID(s) | 426419 |

# Inventory

Primacy Agencies are required to report Inventory data for all water systems.  For GWR reporting a new data element, Outstanding Performers, has been added to the Water System object and the Treatment Process values have been expanded.

This section identifies the following:

- New reporting requirements for Outstanding Performers

- New Code values for Primacy Agencies to identify PWS implementation of 4-log treatment of viruses

- New Code values for Primacy Agencies to identify Purchased Source 4-log treatment of viruses by the seller

- Policies and general coding instructions, including examples, of Primacy Agency reporting of sources of water, treatment plants, flow of the water sources to treatment plants, and treatments applied.

## Outstanding Performers

The GWR and Interim Enhanced Surface Water Treatment Rule (IESWTR) set the frequency of sanitary survey based on water system federal type.  Primacy Agencies must conduct sanitary surveys at least every 3 years for community systems and every 5 years for non-community systems.  If the Primacy Agency determines a community system is an Outstanding Performer, the frequency of sanitary survey may be reduced to every 5 years.

By maintaining Outstanding Performers information, EPA may better keep the public informed about the Outstanding Performers and the role they play in promoting safe drinking water.  Primacy Agencies which reduce the frequency of sanitary surveys for Outstanding Performers must report all water systems which are Outstanding Performers to EPA along with the date of the determination.  Optionally, primacy agencies may report if a water system is not an Outstanding Performer.

Two data elements, Outstanding Performer Code and Outstanding Performer Date, are being added to the Water System object as outlined in Exhibit 58.  The Outstanding Performer Code is optional and if reported must have permitted values N or Y.  The Outstanding Performer Date must be earlier or same as the current date and is conditionally mandatory if the Outstanding Performer Code is reported.

| Exhibit 58: Outstanding Performers Data Elements for Water System Object |
| --- |
| Element Name | Optionality | Domain | Length/ Precision |
| Outstanding Performer Code | Optional | AN | 1 |
| Outstanding Performer Date | Conditional | YYYYMMDD | 8 |

## Treatment Processes

The GWR sets monitoring requirements based upon the absence or presence of 4-log treatment of viruses.  Explicitly reporting presence of this treatment to SDWIS/FED is necessary for PWSS program oversight, as currently, no single treatment process or combination of processes may be used to infer if 4-log treatment of viruses is provided.

Report this information using a treatment process for water systems directly applying the treatment; and a seller source treatment code for water systems purchasing water treated with 4-log treatment of viruses.

Treatment Objective/Processes Applied at PWS

For water systems directly applying 4-log treatment of viruses, treatment process code 361(4-log treatment of viruses) must be paired with the Disinfectant treatment objective. Therefore, Primacy Agencies must report the following data to identify water systems implementing 4-log treatment of viruses:

Treatment Objective:	D

Treatment Process:	361

| Exhibit 59: Required Treatment Process Code |
| --- |
| Code | Description |
| 361 | 4-log treatment of viruses |

Treatment Applied by Seller for a Purchased Water Source

Primacy Agencies must report certain treatments provided by the seller as the seller source treatment code for all purchase sources (consecutive connections and non-purchased).  Seller Source Treatment Code “G” (Treated by seller including 4-log treatment of viruses for GWR) denotes treatment of ground water sources to provide 4-log treatment of viruses

| Exhibit 60: Required Seller Source Treatment Code in WSF Source Object |
| --- |
| Code | Description | Water Type |
| G | Treated by seller including 4-log virus for GWR | GW |

The following decision process is suggested for identifying the proper value to enter in this data element (Seller Source Treatment Code in the Water System Facility Source object):

- No treatment provided by seller (regardless of water type)--Not Treated by Seller; value = ‘N’

- If source is surface water or ground water under the direct influence of surface water,

  - Treated by seller including surface water treatment regulation required filtration, value = ‘F’

  - Treated by seller not including filtration, value = 'Y'

- If source is ground water,

  - Treated by seller including 4-log treatment of viruses, value = ‘G’

  - Treated by seller not including 4-log treatment of viruses, value = 'Y'

Generic Reporting for Sources, Treatment Plants, Flows, Treatments

Primacy Agencies are required to identify and report all sources of drinking water (those controlled by the PWS as well as those purchased by the PWS) to EPA’s SDWIS/FED database, using the Water System Facility Source object.  In addition, Primacy Agencies must report all treatments applied to the sources of water by the PWS with the use of a Water System Facility Treatment Plant object.  Several data elements are required to be reported to characterize treatments applied to purchased water sources by the seller prior to any additional treatments that may be implemented by the purchasing water system.  Further, linkages between Water System Facility Source objects and Water System Facility Treatment Plant objects must be made using the Facility Flow object.  Finally, the treatments implemented/applied by the PWS at the treatment plants must be encoded using the Treatment Data object.  The narrative below reiterates EPA’s policy for reporting sources of water and their treatments, including those sources of water purchased from other Public Water Systems (known as Purchased Sources).  Exhibits 62 to 64 identify the data elements to be reported for Sources of Water (purchased or not), treatment plants, facility flows between sources and treatment plants, and treatments, respectively.

The following rules apply to source, treatment plant and treatment reporting:

- All treatment detail records must be reported to SDWIS/FED associated with treatment plant records, regardless of whether the treatment is occurring at a large treatment plant or is a small building in which disinfectant is added.

- Primacy Agencies may only report treatment data for treatment plant type water system facilities.

- Primacy Agencies must provide information to allow SDWIS/FED to link the source records to the treatment plant records as water system facility flows.

- For consecutive connections, EPA is aware of the complex relationships that may exist between water systems and their treatment. For the purchasing water system, EPA requires reporting whether the seller is partially treating the source as outlined above, filtering a surface water source, providing 4-log treatment of viruses for a ground water source or not providing any treatment. Any buyer treatment must be reported as outlined above. Treatment provide by Sellers must be reported with the Sellers treatment plant inventory.

- Explicit reporting of “no treatment” for a source is required to explicitly confirm that the source is not treated in the Source Treated Code element.

For additional information regarding the reporting of Water System, Water System Facility Source, Water System Facility Treatment Plant, Facility Flow and Treatment Data objects, refer to the most current SDWIS/FedRep Requirements document.

| Exhibit 61: Water System Object Element Optionality |
| --- |
| Element Name | Optionality |
| PWS ID | Required |
| PWS Type | Required |
| PWS Name | Required |
| Activity Flag | Required |
| Deactivation Date | Conditional |
| Wholesale of Water | Optional |
| Retail Population Served | Required |
| Retail Service Connections | Required |
| Non-Community Season Begin (Month And Day) | Conditional |
| Non-Community Season End (Month And Day) | Conditional |
| Owner Type | Required |
| Source Water Protection Code | Optional |
| Source Water Protection Date | Conditional |
| Outstanding Performer Code | Optional |
| Outstanding Performer Date | Conditional |

| Exhibit 62: Source WSF Object Element Optionality |
| --- |
| Element Name | Optionality |
| PWS ID | Required |
| Facility ID | Required |
| Activity Flag | Required |
| Deactivation Date Facility | Conditional |
| Facility Name | Required |
| State Database Facility ID | Optional |
| Facility Type Code | Required |
| Facility Water Type Code | Required |
| Availability | Required |
| Seller PWS ID | Conditional |
| Seller Source Treatment Code | Conditional |
| Source Treated Code | Conditional |
| Reported Filtration Status Code | Conditional |

| Exhibit 63: SDWIS/FED Water Sources and Codes |
| --- |
| Facility Type Code | Description | Permissible Facility Water Type Codes |
| IN | Intake | Surface Water |
| WL | Well | Ground Water (GW), GWUDI (GU) |
| RC | Roof Catchment | Ground Water (GW) |
| SP | Spring | Surface (SW), Ground (GW), GWUDI (GU) |
| IG | Infiltration Gallery | Surface (SW), GWUDI (GU) |
| RS | Reservoir | Surface (SW) |
| NP | Non-piped | Surface (SW), Ground (GW), GWUDI (GU) |
| CC | Consecutive Connection | Surface (SW), Ground (GW), GWUDI (GU) |

Specific reporting requirements exist for purchased sources of water.  These are identified in the Water System Facility Source object with a Facility Type Code element value of either “CC” or “NP”.  The following Water System Facility Source object elements must be valued:

| Exhibit 64: Purchased Source Seller Source Treatment Code Permitted Values |
| --- |
| Element | Description | Permissible Code Values |
| Seller Source Treatment Code | Indicates whether the seller is or is not treating the source or whether the seller treatment status is unknown. | Not treated ( ‘N’ SWTR Filtration ( ‘F’ (for SW and GUI sources) 4-log treatment of viruses ( ‘G’ for GW sources Partial treatment ( ‘Y’ |

All treatment applied to sources of drinking water must also be reported by Primacy Agencies. If a source of water is not treated, Primacy Agencies must affirm that as well. Treatment is reported via a Treatment Plant facility record. Finally, the Primacy Agency must report a linkage between the source of water facility and treatment plant facility.

The following identifies the method to be used to meet the SDWIS/FED reporting requirement for linking Water System Facility Source objects and Water System Facility Treatment Plant objects

- Use the Facility Flow object which

  - Requires

    - PWS ID,

    - Facility ID From element to identify the Water System Facility Source object that is being treated at the treatment plant, and

    - Facility ID To element to identify the Water System Facility Treatment Plant object the source(s) flow to, and

  - Prohibits linkage between a facility (source, treatment plant, etc.) and itself; and

  - Prohibits duplicate links between a specific source and treatment plant combination.

In summary, the Primacy Agency must report all sources of water, all treatment, assign the treatment to a treatment plant record, and link the source records to the treatment plant records. With regard to SWTR reporting, it must also inform EPA of decisions made on unfiltered surface water sources and ground water under the influence of surface water on ground water sources.

WSF Source, WSF Treatment Plant, Treatment Data, Facility Flows

The exhibits in this section provide general examples for reporting for a large water system, PW1234567, with the following WSF sources, WSF treatment plants, treatment data and facility flows:

- Five permanent sources of water (sources 1-5), including

- One purchased from another water system (Source 2-CC02),

- One emergency source (Source 6-WL06), and

- Treatment Plant 1 (TP1) provides 4-log treatment of viruses, and treats Sources 1-3

- Treatment Plant 2 (TP2) has only one treatment, disinfection using gaseous chlorination and treats Sources 4 and 5 are treated

- Source 6, an emergency source, is not treated.

- PW1234567 is an outstanding performer.

| Exhibit 65: Water System Object Elements |
| --- |
| Element Name | Data Value |
| PWS ID | PA1234567 |
| PWS Type | C |
| PWS Name | Anytown USA |
| Activity Flag | A |
| Deactivation Date | Do Not Report |
| Wholesale of water |  |
| Retail Population Served | 100000 |
| Retail Service Connections | 25000 |
| Non-Community Season Begin (Month And Day) | Do Not Report |
| Non-Community Season End (Month And Day) | Do Not Report |
| Owner Type | L |
| Source Water Protection Code | Y |
| Source Water Protection Date | 2007-10-02 |
| Outstanding Performer Code | Y |
| Outstanding Performer Date | 2011-12-12 |

| Exhibit 66: Source Facilities |
| --- |
| Element Name | Source 1 | Source 2 | Source 3 | Source 4 | Source 5 | Source 6 |
| PWS ID | PA1234567 | PA1234567 | PA1234567 | PA1234567 | PA1234567 | PA1234567 |
| Facility ID | IN01 | CC02 | WL03 | WL04 | WL05 | WL06 |
| Activity Flag | A | A | A | A | A | A |
| Deactivation Date Facility |  |  |  |  |  |  |
| Facility Name | Source1 | Source 2 | Source 3 | Source 4 | Source 5 | Source 6 |
| State Database Facility ID |  |  |  |  |  |  |
| Facility Type Code | IN | CC | WL | WL | WL | WL |
| Facility Water Type Code | SW | SW | GU | GW | GW | GW |
| Availability | P | P | P | P | P | E |
| Seller PWS ID |  | PA7654321 |  |  |  |  |
| Seller Source Treatment Code |  | N |  |  |  |  |
| Source Treated Code |  |  |  |  |  | N |
| Reported Filtration Status Code |  |  |  |  |  |  |

| Exhibit 67: Treatment Plant Facilities |
| --- |
| Element Name | Treatment Plant1 | Treatment Plant 2 |
| PWS ID | PA1234567 | PA1234567 |
| Facility ID | TP1 | TP2 |
| Activity Flag | A | A |
| Deactivation Date Facility |  |  |
| Facility Name | Treatment Plant 1 | Treatment Plant 2 |
| State Database Facility ID |  |  |
| Facility Type Code | TP | TP |
| Facility Water Type Code | Do Not Report | Do Not Report |
| Availability | Do Not Report | Do Not Report |
| Seller PWS ID | Do Not Report | Do Not Report |
| Seller Source Treatment Code | Do Not Report | Do Not Report |
| Source Treated Code | Do Not Report | Do Not Report |
| Reported Filtration Status Code | Do Not Report | Do Not Report |

| Exhibit 68: Treatment Data |
| --- |
| Element | Treatment Plant 1 | Treatment Plant 2 |
| PWS ID | PA1234567 | PA1234567 |
| Facility ID | TP1 | TP2 |
| Treatment ID | TT1 | TT2 |
| Treatment Objective | D | D |
| Treatment Process | 361 | 403 |
| Treatment Comments |  |  |

| Exhibit 69: Facility Flows |
| --- |
|  | PWS ID | Facility ID Flow From | Facility ID Flow To |
| Source 1 | PA1234567 | IN01 | TP1 |
| Source 2 | PA1234567 | CC02 | TP1 |
| Source 3 | PA1234567 | WL03 | TP1 |
| Source 4 | PA1234567 | WL04 | TP2 |
| Source 5 | PA1234567 | WL05 | TP2 |

# Other Actions

In addition to the Violation object reporting in Section 2, GWR Actions domain reporting includes Sanitary Surveys reported using the Site Visit object and Corrective Actions reported using the Event Schedule Activity object.

## Sanitary Survey

Under the Ground Water Rule, primacy agencies are required to conduct sanitary surveys on all water systems with ground water sources, and the survey must include an evaluation of eight categories.  Sanitary surveys are reported using the Site Visit object which is part of the Actions Subject Area.  Optionally, primacy agencies may report other types of site visits, including sanitary survey follow-ups.

A finished sanitary survey is one where all eight applicable categories have been evaluated for the entire water system.  For reporting purposes, a finished sanitary survey (code SNSV) means the date a sanitary survey visit was conducted in which all eight sanitary survey components have been evaluated for the entire water system according to the requirements of 40 CFR 141.401(c).

A partial sanitary survey is one where all eight applicable categories have not been evaluated for the entire water system.  A partial sanitary survey (code SNSP) means not all eight sanitary survey components were evaluated for the entire water system.  When a sanitary survey is conducted in multiple visits, (that is, not over consecutive days), the primacy agency must report each visit using the SNSP code and the last visit as finished using the SNSV code.

All finished and partial sanitary surveys conducted for ground water systems must be reported and include the evaluation for each of the eight required categories.  This could include a category being reported as either X- Not Evaluated or Z – Not Applicable.  When a sanitary survey (partial or finished) is conducted over multiple consecutive days, the primacy agency may report this as a single visit, using the last date of the visit.

The following exhibits list the Site Visit object elements, permitted values for Visit Reason, Visit Agency Type and all the Category Evaluations.  Additional data details are provided in SDWIS/FedRep Requirements documentation.

| Exhibit 70: Site Visit Object Elements |
| --- |
| Element Name | Optionality |
| PWS ID | Required |
| Visit ID | Required |
| Visit Date | Required |
| Visit Reason | Required |
| Visit Agency Type | Required |
| Category Evaluation Management and Operations | Conditionally Mandatory * |
| Category Evaluation Source | Conditionally Mandatory * |
| Category Evaluation Pumps | Conditionally Mandatory * |
| Category Evaluation Operator Compliance | Conditionally Mandatory * |
| Category Evaluation Monitoring and Reporting Data Verification | Conditionally Mandatory * |
| Category Evaluation Treatment | Conditionally Mandatory * |
| Category Evaluation Finished Water Storage | Conditionally Mandatory * |
| Category Evaluation Distribution | Conditionally Mandatory * |
| Category Evaluation Security | Optional |
| Category Evaluation Other | Optional |
| Category Evaluation Financial | Optional |
| Site Visit Comment | Optional |
| * Conditionally Mandatory where Visit Reason Code for Sanitary Survey is ‘SNSV’, ‘SSVF’, or ‘SNSP’ and Visit Date is after 11/30/2009 |

| Exhibit 71: Site Visit Object Visit Type Permitted Values |
| --- |
| Code | Description |
| CAPD | Capacity Development Assessment |
| CMPA | Compliance Assistance |
| CNST | Construction Inspection |
| CPEV | Comprehensive Performance Evaluation (CPE) |
| EMRG | Emergency Assistance |
| ENGR | Engineering Determination/Advice/Plan Review |
| FENF | Formal Enforcement |
| FUFE | Follow-up to Formal Enforcement |
| IENF | Informal Enforcement |
| INFI | Informal System Inspection |
| INVG | Investigation (Complaint/Violation/etc.) |
| LABC | Laboratory Certification |
| LABI | Laboratory Inspection |
| LOCD | Locational Data Collection |
| NEED | Needs Survey |
| OM | Operation and Maintenance |
| OTHR | Other |
| PRMT | Permit (Qualification/Review/Compliance) |
| PUBH | Public Hearing |
| RCDR | Record Review |
| RSCH | Regularly Scheduled |
| SHAZ | Sanitary Hazards Investigation |
| SITE | Site Inspection |
| SMPL | Sample Collection |
| SNSV | Sanitary Survey, Finished |
| SNSP | Sanitary Survey, Partial |
| SRCE | Source Water Inspection |
| SRF | State Revolving Fund |
| SSVF | Sanitary Survey Follow-up |
| TECH | Technical Assistance (Non-Specific) |
| TRNG | Training |
| TRTP | Water Treatment Plant Site Visit |
| VAEX | Variance/Exemption related |
| WHPP | Wellhead Protection Program |
| WSHD | Watershed Evaluation |
| XCON | Cross Connection Inspection/Investigation |

| Exhibit 72: Visit Agency Type Permitted Values |
| --- |
| Code | Description |
| AR | Alaskan Remote Village |
| AT | Authority |
| BR | Borough |
| CM | Commission |
| CN | County |
| CT | City |
| DS | District |
| FD | Federal |
| MN | Municipality |
| NA | Native American Tribe |
| PR | Parish |
| RG | Region |
| SA | State Administrative District |
| SD | School District |
| SR | State Administrative Region |
| ST | State |
| TW | Town |
| WD | Water District |

| Exhibit 73: Category Evaluation Permitted Values |
| --- |
| Code | Description |
| M | Minor deficiencies |
| N | No deficiencies or recommendations |
| R | Recommendations made |
| S | Significant deficiencies |
| X | Not Evaluated |
| Z | Not Applicable |

Sanitary Survey Examples

The following examples illustrate GWR sanitary survey scenarios and show the Site Visit details to be reported by the Primacy Agency to EPA.

### Example 1 – Purchase Water System without Treatment or Finished Water Storage

Golden Age MHP, PA9876543, is a community system serving 500 people. Golden Age MHP purchases ground water from PA1234567 and does not provide additional treatment nor does it have finished water storage.  A sanitary survey was conducted on 01/22/2010 by personnel from the county health department.  A significant deficiency in the pumps and a recommendation to exercise the distribution system valves were discussed with the owner during the survey.  There were no other negative findings.

This sanitary survey is reported as finished using code SNSV. All eight categories must be reported; two are reported as Z-Not Applicable (Exhibit 74 Ex 1).

| Exhibit 74 Ex 1: Purchase Water System without Treatment or Finished Water Storage Site Visit Object Elements |
| --- |
| Element Name | Data Value |
| PWS ID | PA9876543 |
| Visit ID | 3585 |
| Visit Date | 2010-01-22 |
| Visit Reason | SNSV |
| Visit Agency Type | CN |
| Category Evaluation Management and Operations | N |
| Category Evaluation Source | N |
| Category Evaluation Pumps | S |
| Category Evaluation Operator Compliance | N |
| Category Evaluation Monitoring and Reporting Data Verification | N |
| Category Evaluation Treatment | Z |
| Category Evaluation Security | N |
| Category Evaluation Other | Z |
| Category Evaluation Finished Water Storage | Z |
| Category Evaluation Distribution | R |
| Category Evaluation Financial | N |
| Site Visit Comment | Optional |

### Example 2 – Large Ground Water System with Ten Wells with Two Partial Sanitary Surveys not on Consecutive Days

Nice Town, PA6479339, is a community system serving 230,000 people.  Nice Town has 10 wells which are treated at four treatment plants.

- A sanitary survey conducted on 02/07/2010 by personnel from one of the state's administrative regions included review of the wells, pumps and finished water storage.

- A significant deficiency with two of the wells and a recommendation to exercise back up pumps were recorded with the operator.

- A second visit conducted on 08/19/2011 by personnel from one of the state's administrative regions included evaluation of the remaining categories.

- During the second visit the operator was informed of a minor deficiency at the treatment plant.

These two partial sanitary surveys must be reported separately using code SNSP. All eight categories must be reported; one is reported as Z-Not Applicable, those not evaluated are reported as X-Not Evaluated.  All eight required categories must be reported as evaluated (M- Minor deficiencies N- No deficiencies or recommendations, R- Recommendations made, or S-Significant deficiencies) in one or the other of the visits (Exhibit 75 Ex 2-A and Exhibit 76 Ex 2-B).

| Exhibit 75 Ex 2-A: Visit Object Elements for Large Ground Water System with Ten Wells Reported as First of Two Visits |
| --- |
| Element Name | Data Value |
| PWS ID | PA6479339 |
| Visit ID | 8543 |
| Visit Date | 2010-02-07 |
| Visit Reason | SNSP |
| Visit Agency Type | SR |
| Category Evaluation Management and Operations | X |
| Category Evaluation Source | S |
| Category Evaluation Pumps | R |
| Category Evaluation Operator Compliance | X |
| Category Evaluation Monitoring and Reporting Data Verification | X |
| Category Evaluation Treatment | X |
| Category Evaluation Finished Water Storage | N |
| Category Evaluation Distribution | X |
| Category Evaluation Security | X |
| Category Evaluation Other | Z |
| Category Evaluation Financial | X |
| Site Visit Comment | Optional |

| Exhibit 76 Ex 2-B: Site Visit Object Elements for Large Ground Water System with Ten Wells Reported as Second of Two Visits |
| --- |
| Element Name | Data Value |
| PWS ID | PA6479339 |
| Visit ID | 8543 |
| Visit Date | 2011-08-19 |
| Visit Reason | SNSP |
| Visit Agency Type | SR |
| Category Evaluation Management and Operations | N |
| Category Evaluation Source | X |
| Category Evaluation Pumps | X |
| Category Evaluation Operator Compliance | N |
| Category Evaluation Monitoring and Reporting Data Verification | N |
| Category Evaluation Treatment | M |
| Category Evaluation Finished Water Storage | X |
| Category Evaluation Distribution | N |
| Category Evaluation Security | N |
| Category Evaluation Other | Z |
| Category Evaluation Financial | N |
| Site Visit Comment | Optional |

## Corrective Actions

Water systems with significant deficiencies or fecal indicator positive sources must complete corrective actions as defined in CFR 141.403.  Corrective actions will be reported to SDWIS/FED using Event Schedule Activity object.  A corrective action may have multiple interim schedule dates; however, only the final date for each significant deficiency or fecal indicator positive source water sample event must be reported unless there is a violation incurred for an interim step.  When a violation has been incurred for an interim step, the interim step must be reported as an Event Schedule Activity.

The following exhibits list the Event Schedule Activity object elements, new permitted values for Activity Type Code and Reason Code.  Additional data details are provided in SDWIS/FedRep Requirements documentation.

| Exhibit 77: Event Schedule Activity Object Elements |
| --- |
| Element Name | Optionality for GWR Events | Element Description |
| PWS ID | Required | Public Water System Identifier |
| Event Activity ID | Required | Uniquely identifies the event schedule activity within the water system |
| Activity Type Code | Required | Describes the activity associated with the corrective action |
| Activity Actual/Due Date | Required | Required calendar date by which corrective action must be successfully completed |
| Activity End/Achieved Date | Conditional | Calendar date on which corrective action was successfully completed |
| Reason Code | Conditional | Code value that represents reason this corrective action is required |
| Activity Comment | Optional |  |

| Exhibit 78: Activity Type Code Permitted Values for GWR |
| --- |
| Code | Description |
| SDFF | Significant Deficiency Corrective Action |
| SDFI | Significant Deficiency Interim Step |
| FICF | Fecal Indicator Contamination |
| FICI | Fecal Indicator Contamination Interim Step |

| Exhibit 79: Reason Code Permitted Values for GWR and Optional Surface Water Corrective Actions |
| --- |
| Code | Description |
| GW | Ground Water |
| SH | Subpart H |

The Reason Code for all GWR related corrective actions is GW.  If corrective actions are reported for Subpart H related regulations the reason code must be SH.

Event Schedule Activity Examples

The following examples illustrate GWR corrective action scenarios and show the Event Schedule Activity details to be reported by the Primacy Agency to EPA.

### Example 1 – Significant Deficiency Corrective Actions

PWS PA2154376, is a community system serving 800 people.

- The system has one well in use year-round and does not provide 4-log treatment of viruses before the first customer.

- During a sanitary survey on 09/01/2013, the Primacy Agency identifies a significant deficiency—leaking septic tanks close to the system’s well.

- The system is notified of the deficiency on 09/14/2013 in a letter from the Primacy Agency. The letter does not indicate a specific corrective action that the system is required to take.

- As required, the system contacts the Primacy Agency within 30 days of receiving written notice of the significant deficiency and the system and the Primacy Agency develop a plan for implementing corrective action.

- The first step of the corrective action plan is scheduled to be completed by 12/01/2013 with the remainder scheduled to be completed by 10/01/2014.

- The first step was not completed until 02/25/2014.  All steps were completed on 09/22/2014.

- The scheduled corrective action must be reported (Exhibit 80 Ex 1-A) with the next quarterly actions report without an Activity End/Achieved Date.

- When the interim corrective action step was not completed on time, it must be reported (Exhibit 81 Ex 1-B) with the next quarterly actions report without an Activity End/Achieved Date.  The corrective action is also associated to a type 45 violation (Exhibit 8 Ex 4-A) when the violation is reported.

- The completed interim corrective action step must be reported with an Activity End/Achieved Date (Exhibit 86 Ex 2-C) with the next quarterly actions report.

- The final completed corrective action must be reported with an Activity End/Achieved Date (Exhibit 83 Ex 1-D) with the next quarterly actions report.

| Exhibit 80 Ex 1-A: Significant Deficiency Final Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA2154376 |
| Event Activity | 648 |
| Activity Type Code | SDFF |
| Activity Actual/Due Date | 10/01/2014 |
| Activity End/Achieved Date | Do Not Report |
| Reason Code | GW |
| Activity Comment | Optional |

| Exhibit 81 Ex 1-B: Significant Deficiency Interim Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA2154376 |
| Event Activity | 753 |
| Activity Type Code | SDFI |
| Activity Actual/Due Date | 2013-12-01 |
| Activity End/Achieved Date | Do Not Report |
| Reason Code | GW |
| Activity Comment | Optional |

| Exhibit 82 Ex 1-C: Significant Deficiency Interim Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA2154376 |
| Event Activity | 753 |
| Activity Type Code | SDFI |
| Activity Actual/Due Date | 2013-12-01 |
| Activity End/Achieved Date | 2014-02-25 |
| Reason Code | GW |
| Activity Comment | Optional |

| Exhibit 83 Ex 1-D: Significant Deficiency Completed Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA2154376 |
| Event Activity | 648 |
| Activity Type Code | SDFF |
| Activity Actual/Due Date | 10/01/2014 |
| Activity End/Achieved Date | 09/30/2014 |
| Reason Code | GW |
| Activity Comment | Optional |

### Example 2 – Fecal Indicator Positive Source

PWS PA7654721 is a non-community GWS serving 8,000 people.

- The system has three wells in use year-round and does not provide 4-log treatment of viruses before the first customer.

- TCR sampling performed during the month of June 2015 resulted in a total coliform-positive (TC+) result.

- The PWS is notified about the TC+ result on 6/10/2015 and performs triggered source water monitoring within 24 hours.

- Fecal indicator-positive (FI+) triggered results from Well #1 and Well #2 were reported to the system.

- The system receives notification that the additional monitoring sample results are FI+ on 06/19/2015.

- The system consulted the Primacy Agency within 30 days and agrees to a corrective action plan to provide a single treatment plant for both sources within 120 days, i.e. by 10/17/2015.

- The PWS did not install treatment by 10/17/2015.

- The PWS completed the corrective action by installing treatment on 12/15/2015.

- Two scheduled corrective actions must be reported (Exhibits 84 Ex 2-A and 85 Ex 2-B) with the next quarterly actions report without an Activity End/Achieved Date.  In the example, the Primacy Agency uses the Comment field to identify the source water system facility. Each corrective action is also associated to a type 42 violation (Exhibits 4 Ex 3-A and 5 Ex 3-B) when those violations are reported.

- Two completed corrective actions must be reported (Exhibits 86 Ex 2-C and 87 Ex 2-D) with the next quarterly actions report with an Activity End/Achieved Date.

| Exhibit 84 Ex 2-A: Fecal Indicator Positive Source Scheduled Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA7654721 |
| Event Activity | 128 |
| Activity Type Code | FICF |
| Activity Actual/Due Date | 2015-10-17 |
| Activity End/Achieved Date | Do Not Report |
| Reason Code | GW |
| Activity Comment | Well #1 |

| Exhibit 85 Ex 2-B: Fecal Indicator Positive Source Scheduled Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA7654721 |
| Event Activity | 129 |
| Activity Type Code | FICF |
| Activity Actual/Due Date | 2015-10-17 |
| Activity End/Achieved Date | Do Not Report |
| Reason Code | GW |
| Activity Comment | Well #2 |

| Exhibit 86 Ex 2-C: Fecal Indicator Positive Source Completed Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA7654721 |
| Event Activity | 128 |
| Activity Type Code | FICF |
| Activity Actual/Due Date | 2015-10-17 |
| Activity End/Achieved Date | 2015-12-15 |
| Reason Code | GW |
| Activity Comment | Well #1 |

| Exhibit 87 Ex 2-D: Fecal Indicator Positive Source Completed Corrective Actions Event Schedule Activity Object Elements Reported |
| --- |
| Element Name | Data Value |
| PWS ID | PA7654721 |
| Event Activity | 129 |
| Activity Type Code | FICF |
| Activity Actual/Due Date | 2015-10-17 |
| Activity End/Achieved Date | 2015-12-15 |
| Reason Code | GW |
| Activity Comment | Well #2 |