## Slide 1
Stephen D. Preston
National Water Quality Programs
U.S. Geological Survey
Current and Emerging Tools for the Assessment of Water-Quality Conditions in Waters of the
Conterminous U.S.

## Slide 2
Current and Emerging Tools
* New models for assessing benchmark exceedance probabilities
* New web-based water-quality mapping systems
* New and updated national geospatial data sets
* Updated spatially explicit models for the U.S.
2

## Slide 3
SPARROW Water-Quality Model
SPAtially Referenced Regression on Watershed Attributes)
Model Predictions
3

## Slide 4
2,700 calibration sites with data from 73 agencies
Monitoring Data Are Critical for Modeling
4

## Slide 5
Total Nitrogen Yields and Sources
Yields
Largest Sources
5
Preston, et al (2011) Factors Affecting Stream Nutrient Loads: A Synthesis of Regional SPARROW Model Results for the Continental United States. https://doi.org/10.1111/j.1752-1688.2011.00577.x

## Slide 6: How SPARROW Models Can Inform Nutrient Management Decisions
Chesapeake Bay Priority Agricultural Watersheds
Both TN and TP
TP
TN
Largest Sources of Nitrogen to U.S. Streams
Low
High
Relative Contributions of Phosphorus to the Gulf of Mexico
SPARROW Predictions of Stream Nitrogen Flux
Predict mean-annual flux, yield and concentration for unmonitored streams
Predict contaminant flux to downstream receiving waters such as estuaries
Apportion stream loads to major nutrient sources and upstream watersheds
Provide a framework for prioritizing areas for management actions
Evaluate the potential effects of landscape change scenarios on water quality
6

## Slide 7
SPARROW Model Updates for 2012
NAWQA
SPARROW Modeling Regions
* Expected completion 2019
* Models developed for each of 4 constituents: water balance, nutrients (N&P), sediment
* Models based on improved geospatial data sets
* Models based on NHDPlus (100K) spatial framework
* Models for 5 regions covering the conterminous U.S.
7

## Slide 8
RF1 (1:500,000)
2,462 Reaches
NE SPARROW Enhanced NHD (1:100,000)
42,000 Reaches
NAWQA Cycle 3 SPARROW Modeling
Improved Stream Network Data
8

## Slide 9
NAWQA SPARROW Model Development
Stream Network Data Improvements
9

## Slide 10
10

## Slide 11
NAWQA SPARROW Model Development
Water Balance Models – Statistically Significant Predictors
Sources of Water to Streams
* Runoff – (Precipitation – evapotranspiration)
* Wastewater Discharge (all regions)
* Springflow (most regions)
* Transfers (western regions)
Delivery of Water to Streams
* Vegetation, temperature, soil characteristics, others
Loss of Water from Streams
* Reservoirs – (all regions)
* Losses from Streams (western regions)
* Public Supply (most regions)
* Irrigation (western regions)
11

## Slide 12
NAWQA SPARROW Model Development
Water Balance Models – Preliminary Predictions
Incremental Water Yield (mm/yr)
Delivered Water Yield (mm/yr)
12
Preliminary Information-Subject to Revision. Not for Citation or Distribution

## Slide 13
Tracking Nutrient Loading to the Nation’s Estuaries and Great Lakes
Pacific Northwest
California
Coast
(coming soon)
Gulf of Mexico
Atlantic
Coast
Great Lakes
http://water.usgs.gov/nawqa/sparrow/estuary
13

## Slide 14
NAWQA SPARROW Model Development
Web-based Mapping Tools – Total Dissolved Solids
14
Anning and Flynn (2014) Dissolved-Solids Sources, Loads, Yields, and Concentrations in Streams of the Conterminous United States (https://pubs.usgs.gov/sir/2014/5012/).

## Slide 15
NAWQA SPARROW Model Development
Web-based Mapping Tools – Total Dissolved Solids
15
Anning and Flynn (2014) Dissolved-Solids Sources, Loads, Yields, and Concentrations in Streams of the Conterminous United States (https://pubs.usgs.gov/sir/2014/5012/).

## Slide 16
NAWQA SPARROW Model Development
Web-based Mapping Tools – Total Dissolved Solids
16
Anning and Flynn (2014) Dissolved-Solids Sources, Loads, Yields, and Concentrations in Streams of the Conterminous United States (https://pubs.usgs.gov/sir/2014/5012/).

## Slide 17: Models predict benchmark exceedance probabilities in streams & rivers: pesticides
Stone et al: Watershed Regressions for Pesticides (WARP) models https://cida.usgs.gov/warp/home/
17

## Slide 18: Models predict benchmark exceedance probabilities in groundwater: manganese
Rosecrans and others, 2017, Prediction and visualization of redox conditions in the groundwater of Central Valley, California, Journal of Hydrology; https://doi.org/10.1016/j.jhydrol.2017.01.014
Domestic wells
Public supply wells
Mn > 50 ug/L
Mn > 150 ug/L
Mn > 300 ug/L
Mn > 50 ug/L
Mn > 150 ug/L
Mn > 300 ug/L
18

## Slide 19
Additional Information
Further Details of SPARROW:
http://water.usgs.gov/nawqa/sparrow
Contact Information:
spreston@usgs.gov
19