## Slide 1: LCRR Early Implementation Issues: Monitoring for Lead in Schools and Child Care Facilities ASDWA Annual Conference October 27, 2020

## Slide 2: Outline
Regulatory History
Proposed LCRR Requirements for Schools and Child Care Facilities
Maryland’s Experience
Challenges
Questions/Discussion

## Slide 3: Regulatory History: Schools and Child Care
Lead Contamination Control Act (1988)
  Schools and child care facilities
  EPA list of water fountains/coolers with Lead
  Repair, remove, replace fountains and/or test drinking water (Action Level = 20 ppb, 250 mL)
  EPA Guidance
Notes: 2011 Lead Ban is the Reduction of Lead in Drinking Water Act

## Slide 4: Regulatory History: Schools and Child Care
Lead and Copper Rule (1991) Revisions 2000 & 2007
  Public water systems (CWS and NTNCWS)
    Schools and child care facilities NOT included unless CWS or NTNCWS
  Action Level = 15 ppb (1 L, first-draw)
  Lead and Copper Rule Revisions (proposed 2019)
    Schools and child care facilities included
      Lead sample results not part of CWS 90th percentile calculation
Notes: 2011 Lead Ban is the Reduction of Lead in Drinking Water Act

## Slide 5: LCRR – Schools and Child Care Facilities
Who?
  Community Water Systems, Schools (K-12), licensed child care facilities
What?
  CWS
    Compile list of facilities located within water distribution system
    Contact facilities and provide information (Public Education, 3Ts)
    Collect samples for lead
    Report results to facility, State/Primacy Agency, local health department
    Certify to State/Primacy Agency
  School and child care facility
    Communicate results to parents and occupants
    Take remedial action
    Expand testing (if desired)

## Slide 6: LCRR – Schools and Child Care Facilities
Where?
  Samples collected from drinking water outlets
    Schools – 5 samples
    Child care facilities – 2 samples
When?
  Annually test 20% facilities (i.e. 5 year sampling frequency)
  Annually provide public education
How?
  EPA Technical Guidance (3Ts)
Options
  Waivers (full or partial) for CWS

## Slide 7: LCRR – Schools and Child Care Facilities
  Other Regulatory Options: “Upon Request” Program
    Same components as mandatory program
    Limited to facilities that request testing
    CWS must annually contact facilities
    EPA assumes 5% participation per year in cost estimate

## Slide 8: Maryland’s Program
  Maryland House Bill 270 (2017)
  ALL public, charter, and nonpublic schools
    Mandatory testing
      ALL drinking water outlets
      3 year frequency
      EPA 3Ts protocol
    Elevated results
      Corrective action
      Public notification
      Follow up testing
  Expand program to licensed child care facilities

## Slide 9: LCRR: Challenges
  EPA 3Ts
    no Action Level = no uniformity
    Sampling protocol – different objectives
  Identifying problems - # taps tested
  Inventory - # child care “facilities”
  CWS resources
  Data collection/tracking
  Child care facility licenses
  EPA “upon request” option

## Slide 10: Questions?
Christina Ardito
Maryland Department of the Environment Water Supply Program
www.MDE.maryland.gov
Christina.Ardito@maryland.gov